## Slide 1: Multrans Path Optimization draft-zhou-mboned-multrans-path-optimization-02 Cathy ZHOU <cathy.zhou@huawei.com> Qiong SUN <sunqiong@ctbri.com.cn>
IETF 84, Vancouver

## Slide 2: Scenario
(*, G) Join
TV
IPv4 source
STB
MTR1
HGW
IPv6
MTR(Multicast Translation Router) can be mXlate and mAFTR
Multicast
data Flow
MTR2
IPv4 Router
IPv6 Router
MTR1 has two upstream routers
MRT1 can receive both IPv4 and IPv6 (*.G) Join request.
Problems
  MTR1 needs to select a best path to RP or Source in both IPv4 and IPv6 networks.
  MTR1 needs to send Prune Messages to the worse path, when it receives two multicast data flows in IPv4 and IPv6 interface.
Notes: RFC4601(PIM-SM) chapter 3.6 says
  Using multi-access LANs such as Ethernet for transit is not uncommon in multicast.
  Solution: when duplicate data packets appear on the LAN from different routers, these routers notice this and then elect a single forwarder. This election is performed using PIM Assert messages, which resolve the problem in favor of the upstream router that has (S,G) state; or, if neither or both router has (S,G) state, then the problem is resolved in favor of the router with the best metric to the RP for RP trees, or the best metric to the source to source-specific trees.
Existing IPv4-IPv6 Multicast migration
  draft-lee-behave-v4v6-mcast-fwk-00 Multicast Translator (mXlate)
  draft-ietf-softwire-dslite-multicast-00 Multicast AFTR (mAFTR)
Multi-edge IPv4-IPv6 multicast router
  For robustness, reliability and load distribution purposes, several nodes in the network can embed the mAFTR function
  It is common there are many IPv4 networks and many IPv6 networks that connected to each other, leading to multi-mXlates at the edge of a network.
Both mXlate and mAFTR will have more than one path to reach the RP or source S. Or in other word, they have two upstream routers, one is IPv6 router, and the other is IPv4 router.

## Slide 3: Proposed Solution
When MTR receives two multicast data flows (one from IPv4 interface and the other from IPv6 interface), it compares two flows according to draft-boucadair-behave-64-multicast-address-format to confirm whether they are the same multicast data flow. If they are the same data flows, select one or two.
When MTR receives an IPv6 (S, G) or (*, G) Join, virtual IPv6 Router selects an interface to send Join message. The interface can be IPv6 upstream IF or IPv4 upstream IF (via interface between virtual IPv6 Router and virtual IPv4 Router)
Virtual
IPv4 Router
MTR Router
IPv4 upstream IF
IPv6 upstream IF
Virtual
IPv6 Router
For simplification,
we use two virtual Routers to replace MTR Router

## Slide 4: Select an Interface to the Source
IPv6 Router
IPv4 Router
MTR
Multicast source
(*, G) Join
m1
m2
m3
  If m2>m3+m1, sending PIM Join message from IPv4 interface;
  If m2<m3+m1, sending PIM Join message from IPv6 interface;
Notes:   Set the Metric value m1 for translation or encapsulating from IPv4 multicast to IPv6 multicast data .
  From the interface connecting IPv6 Router, MTR can get the metric m2 to reach S or RP by PIM assert message from IPv6 Router.
  From interface connecting IPv4 Router, MTR can get the metric m3 to reach S or RP by PIM assert message from IPv4 Router.
  When MTR receives an IPv6 PIM Join message, virtual IPv6 Router compares m2 and m3+m1. If m2>m3+m1, sending PIM Join message from IPv4 interface; If m2<m3+m1, sending PIM Join message from IPv6 interface;

## Slide 5: Select a Multicast Data Flow From Upstream IF
IPv6 Router
IPv4 Router
MTR
Multicast source
Multicast flow 1
Multicast flow 2
m2
m3
m1
  If m2>m3+m1, MTR will send PIM Prune Messages to IPv6 interface;
  If m2<m3+m1MTR will send PIM Prune Messages to interface of two virtual Routers. MTR will not translate or encapsulate multicast data from IPv4 to IPv6.
Notes:   MTR gets two multicast flows from IPv6 and IPv4 Router, and two multicast data flow are the same multicast data flows
  If virtual IPv6 Router gets multicast data from interface between two virtual routers, it will compare m2 and m3+m1 (same as last slide).
  If m2>m3+m1, MTR will send PIM Prune Messages to IPv6 interface; If m2<m3+m1MTR will send PIM Prune Messages to interface of two virtual Routers. MTR will not translate or encapsulate multicast data from IPv4 to IPv6.

## Slide 6: Requirements to the Multicast Router
Check multicast data flow from IPv4 and IPv6 interfaces to determine whether they are the same multicast data flows.
Send PIM Assert message from IPv4 and IPv6 interfaces with different Metric value.
May stop translating or encapsulating IPv4 to IPv6 multicast flow or send Prune Messages to stop receiving IPv6/IPv4 multicast flow.

## Slide 7: References
RFC4601
draft-lee-behave-v4v6-mcast-fwk
draft-ietf-softwire-dslite-multicast
draft-ietf-mboned-64-multicast-address-format

## Slide 8: Next Steps
Adopt as WG item?