## Slide 1: IETF MIF & IEEE 802.21
Juan Carlos Zuniga
Subir Das
Yoshihiro Ohba

## Slide 2: Future IETF MIF work (from OMA-MIF Workshop at IETF83)
1) Extend current MIF API to add additional messages for notifications.
2) Write a draft to define requirements for an abstract notifications API.
3) Write an informational draft that provides recommendations about using the MIF API in order to handle interface changes.

## Slide 3: IETF MIF API (@IETF83)
Application Connectivity Management
Application hints that it wants to connect
Application hints that connection is idle
Application hints that connection can be broken
API hints that Interface/PD is going away
API indicates that interface is going away
API indicates that interface is expensive
Etc?

## Slide 4: IEEE 802.21 MIHS (Published in 2008)
Media Independent Handover Services
Provides predictive signaling that can proactively trigger handovers or flow mobility and hence enhance QoE (ES)
Allows a better control of lower layers to enforce Operator and User’s policies (CS)
Provides information about available access networks (IS)
MIHF
MIH User
(MIP, Policy Control, Conn Mngr)
L1
L2 (IF#1)
L2 (IF#2)
L2 (IF#n)
L1
L1
…
MIH_SAP (Service Access Point)
MIH_Link_SAP (Service Access Point)

## Slide 5: IEEE 802.21 MIH_SAP (Published in 2008)
Media Independent Services (partial list)
Link Capability Discovery
Registration
Event Subscription
Link Parameters Report/Get
Link Detected/Up/Down/Going-Down
Link Handover Imminent/Complete
Link Thresholds Configuration
Link Actions
Handover Commit/Complete/Query
Get Information
http://standards.ieee.org/getieee802/download/802.21-2008.pdf

## Slide 6: Recommendations
IETF MIF can take advantage of the work that 802.21 has already done
  802.21 defines a Media Independent Services SAP (e.g. API) that provides some of the functionalities that MIF is looking for
  802.21 also defines low level Media Specific SAPs for the underlying access technologies (lower level)
IETF MIF should make a list of MIF-specific requirements and should reference MIH SAP primitives when appropriate
  Take advantage of lessons learned avoid incompatibilities
  If non-existing functionalities are identified both MIF and 802.21 should work together to define them

## Slide 7
Straw Man Proposal

## Slide 8: IETF MIF API
MIF API
Application
IF1
IF2
IFn
…
High Level API
Communications API
Network Link API

## Slide 9: MIF API – Straw Man Proposal (1)
MIF API
Application
IF1
IF2
IFn
…
Communications API
Network Link API
Connection Manager
High Level API
MIHF

## Slide 10: MIF API – Straw Man Proposal (2)
MIF API
Application
IF1
IF2
IFn
…
MIHF
Communications API
Network Link API
Connection Manager
High Level API

## Slide 11: Discussion
Should MIF API propose abstract messages and simply explain that a specific instantiation of some of them is described in the MIH SAP?
Should MIF API expose different primitives and translate to MIH_SAP or expose directly MIH_SAP or use the same name?