## Slide 1: IPv6 RA Options for Multiple Interface Next Hop Routes
Behcet Sarikaya(sarikaya@ieee.org)
IETF 84
draft-sarikaya-mif-6man-ra-route-01

## Slide 2: RA Route Option Motivation
RFC 4191 defines Route Information Option
  Prf field is to prefer the router associated with this IPv6 destination prefix
  Next hop address is missing
  Next hop address metric is missing
Metric field
  is added (preference for Next Hop Address) to the Route Information Option and the new option is called Route Prefix Option
Next Hop Address option
  Next hop address represents the IPv6 destination prefixes reachable via the given next hop
  Next hop address metric to prefer the next hop associated with this IPv6 destination prefix over others, when multiple identical prefixes (for different next hops) have been received

## Slide 3: RA Route Option Motivation - Continued
Next Hop Address with Route Prefix option
  Includes next hop with RPO in one option to designate that specific routes are available via routers
  If there is more than one route available via specific next hop, one next hop which contains multiple route prefix options
RA based solution
  Assume clients that know what to do with the info
  Those that don’t simply ignore

## Slide 4: Proposed RA Options
RPO
  Defines the destination prefix
  Borrows from RFC4191 in using the Reserved and Prf values
  Adds metric in place of resvd
  Prf is for preferring the router and metric is for preferring the next hop
Next Hop Address
  Defines IPv6 next hop address.

## Slide 5: Proposed RA Options
Next Hop Address and RPO
  Defines the two options together in one option

## Slide 6: Mailing List Discussions
Feedback from WG:
Brian commented that a central site-wide configuration mechanism is needed
Zhen asked how to relate the prefix option with nexthop option if they are used combined
To clearly indicate the next hop address associated with the right RPO, to avoid any inconsistency arising from sending the two in two different options
Hui asked what is the problem with RFC 4191?
No problem with 4191 however multiple interfaced smart phones and multi-homed hosts bring the need to add a few new RA options
Ok to progress into WG draft?