## Slide 1: 3D Video in the Session Description Protocol (SDP) draft-capelastegui-mmusic-3dv-sdp-00
Pedro Capelastegui
capelastegui@dit.upm.es

## Slide 2: 3D Video in SDP
Goal: Describe 3D video streams in SDP
3DV stream:
  Composed of 2+ streams: views, depth maps
  3DV format options: simulcast, video-plus-depth, frame-packing
Extension requirements:
  3DV format negotiation
  Relationship between views/maps of 3DV stream

## Slide 3: Additions to SDP
New media-level attribute: “3dvFormat”
  3D format for a media description
  Associated to media format (payload type number)
  Four defined formats
  a=3dvFormat:<fmt> <attribute>:<value>
New decoding dependency [RFC 5583]: “3dd”
  Dependency between views/maps in 3DV stream
  A “DDP” group represents a single 3DV stream
Notes: By comparison, draft-ietf-mmusic-signal-3d-format-00 adds:
New media-level attribute “3dFormat”
New SDP grouping “3DS”
However, negotiation is quite different between drafts:
In draft-ietf-mmusic-signal-3d-format-00, a 3DS group represents a single 3D format option for a 3D stream. If multiple 3D formats are offered, the SDP must include multiple 3DS groups and multiple media descriptions, of which the answerer selects those with the preferred 3D format
In draft-capelastegui-mmusic-3dv-sdp-00, a 3dd group represents a 3D stream (including all 3D formats). If multiple 3D formats are offered, new media formats must be added to the media descriptions in the 3D stream. The answerer’s selection of media formats must comply with the restrictions imposed by “a=depend” attributes.

## Slide 4: SDP Example
a=group:DDP 1 2
m=video 1111 RTP/AVP 99 100
a=rtpmap:99 H264/90000
a=3dvFormat:99 stereo-view:left
a=rtpmap:100 H264/90000
a=3dvFormat:100 frame-pack:side-by-side
a=mid:1
m=video 1112 RTP/AVP 99 100 101
a=rtpmap:99 H264/90000
a=3dvFormat:99 depth-map-metadata:1
a=rtpmap:100 H264/90000
a=3dvFormat:100 depth-map-simulcast:1
a=rtpmap:101 H264/90000
a=3dvFormat:101 stereo-view:right
a=mid:2
a=depend:99 3dd 1:99; 100 3dd 1:99; 101 3dd 1:99
2 media descriptions, 5 3D configurations
2D video
  fmt: 99,0
Frame-packing
  fmt: 100, 0
Video-plus-depth
  fmt: 99, 99
Simulcast, view + depth map:
  fmt: 99, 100
Simulcast, 2 views
  fmt: 99, 101
Notes: Offer with multiple 3D format highlights differences between drafts. A similar offer using draft-ietf-mmusic-signal-3d-format-00 would require ~8 media descriptions.