## Slide 1: Trafficclass Attribute in SDP at IETF84
draft-ietf-mmusic-traffic-class-for-sdp-02
1 August 12
James Polk
Subha Dhesikan
Paul Jones

## Slide 2: What this Draft is About
Traffic Classification attribute of sessions for
  Policy decisions based on type of traffic within session
  Monitoring specific types of traffic across network
  DSCP marking (individual or in groups)
  Network resource allocations
  Etc
Labels originated within RFC 4594
  “not just RTP, or port #, but which type of video”?
RSVP App-ID Object defined in RFC 2872
  TSVWG ID defines profiles
    WG hummed 100% for adoption, but not yet WG item

## Slide 3: Individual Component Parts
Categories
Conversational
Multimedia Conferencing
Real-Time Interactive
Multimedia Streaming
Broadcast
Applications
Audio
Video
Text
application-sharing
Presentation-data
Whiteboarding
Webchat/IM
Gaming
Virtualized-desktop
Remote-desktop
Telemetry (e.g., NORAD missile control)
Multiplex (i.e., combined streams)
Webcast
IPTV
Live-events (though not the buffered ones)
Surveillance
Adjectives
Immersive
avconf
Realtime-Text
Web
aq
admitted
nonadmitted
none

## Slide 4: What else changed in WG-02
converged the use of terms 'parent' and 'category' to just 'category' for consistency.
changed ABNF to reflect extensibility by not having applications and adjectives named in the ABNF, rather have them merely IANA registered.
  (Paul isn’t satisfied yet)
merged the qualified and unqualified adjective sections into a single section on adjectives, but allowing some to have a preceding qualifier.
general clean-up of the doc.

## Slide 5: What wasn’t done in WG-02
add more to the 'how does this get processed' portion of Section 3. That will come in the next revision.
Need clearer sections on each component
  Category
  Application
  Adjective
Will recommend which components belong together, i.e.,
  Which applications belong with which categories
  Which adjectives belong with which applications

## Slide 6: Open Issue #1 – ABNF (still)
attribute =/ traffic-class-label
traffic-class-label = "trafficclass" ":" [SP] category
"." application *( "." adjective )
category = "Broadcast" /
"Realtime-Interactive" /
"Multimedia-Conferencing" /
"Multimedia-Streaming" /
"Conversational" / tcl-token
application = tcl-token
adjective = classified-adjective /
unclassified-adjective
classified-adjective = tcl-token ":" tcl-token
unclassified-adjective = tcl-token
tcl-token = %2D / %30-%39 / %41-%5A / %61-7A

## Slide 7: Open Issue #2 – RFC 6648
framework of traffic label, now:
RFC 6648 is BCP removing non-standard alpha prefixes
  Meaning no more “_”
  Is this acceptable to WG?
a=trafficclass Category.application.adjective(s)._foo._bar
delimiter
Proprietary delimiter

## Slide 8: What’s next?
Need more reviewers