## Slide 1: Multiple LDP Instances in single Label Space Mustapha Aïssaoui, Pranjal K. Dutta Alcatel-Lucent
IETF 84, July 2012
Slide <number>
Notes: <number>

## Slide 2: Motivation
IETF 84, July 2012
Slide <number>
Enables fate separation of various LDP FEC types across the verticals - control plane and data plane.
Requirements from operators esp. on fate separation of control planes for IPV4 and IPV6 Transport Tunnels in LDP. Extensive discussion in mailing list on this requirement in the context of LDP IPV6.
Another example could be control plane separation of PW FEC types and Multi-Point LDP FEC types from existing IPV4 FEC Types.
Notes: <number>

## Slide 3: Solution
Run multiple parallel sessions between two peering network nodes.
Each session uses a unique LSR-ID. Single network node hosts multiple LSR-IDs.
Multiple of such LSRs in the node share same label space, ILM, FTN etc.
Backward compatible with all procedures in RFC 5036 and existing protocol rules apply as is.
IETF 84, July 2012
Slide <number>
Notes: <number>

## Slide 4: Solution (Contd.)
Each multi-LSR peering sessions MUST use separate transport address.
The FEC label mappings advertised over parallel sessions MUST be disjoint from one another. Use LDP session capabilities to make them disjoint.
Use LDP Adjacency Capabilities for fate separation in data plane if required. Otherwise dedicate separate links for selected FEC types.
IETF 84, July 2012
Slide <number>
Notes: <number>

## Slide 5: Solution (Contd.)
While running multi-instance LDP peering between two nodes, it is possible that all such sessions would distribute same set of local addresses in each node through Address Message.
An implementation MAY segregate the local address space in each node among the multiple ldp instances to avoid duplication of address distribution.
IETF 84, July 2012
Slide <number>
Notes: <number>

## Slide 6: Example 1
IETF 84, July 2012
Slide <number>
2
1
Both the interfaces 1 and 2 are dual-stack (IPV4 and IPV6) interfaces. Alternately Interface 1 can be IPV4 only and Interface 2 can be IPV6 only.
LDP instance with peering LSR-A1:0 and LSR-B1:0 is dedicated for IPV4 FEC types. Interface 1 is added to instance and hellos are
exchanged using IPV4.
LDP instance with peering LSR-A2:0 and LSR-B2:0 is dedicated for IPV6 FEC types. Interface 2 is added to instance and hellos are
exchanged using IPV6.
A
B
LSR-A1:0
LSR-A2:0
LSR-B1:0
LSR-B2:0
Notes: <number>

## Slide 7: Example 2
IETF 84, July 2012
Slide <number>
2
1
Both the interfaces 1 and 2 part on LDP instance with peering session between LSR-A1:0 and LSR-B1:0. This session is dedicated for all transport FEC types (IPV4, Multi-point etc).
LDP instance with peering LSR-A2:0 and LSR-B2:0 is dedicated for PW FEC Types. The peering session is triggered by t-LDP adjacency between LSR-A2:0 and LSR-B:0.
A
B
LSR-A1:0
LSR-A2:0
LSR-B1:0
LSR-B2:0
t-LDP Adj.
Notes: <number>

## Slide 8: Thank you!
We are looking forward to review and comments in mailing list.