## Slide 1: Open Issues in draft-ietf-mpls-ldp-ipv6-07 Pranjal K. Dutta, Mustapha Aïssaoui, Matthew Bocci, Wim Henderickx Alcatel-Lucent
IETF 84, July 2012
Slide <number>
Notes: <number>

## Slide 2: Backward Compatibility of FEC Resolution with RFC 5036/5283
IETF 84, July 2012
Slide <number>
Current version of LDP IPv6 draft ties the FEC types resolved over a given link to the type of adjacency over that link. Misinterprets section 2.7 in RFC 5036.
  IPv4 (IPv6) FEC require an IPv4 (IPv6) adjacency before being advertised and resolved (Ref. Section 7)
  This resulted in the draft requiring to maintain a separate Hello adjacency for each of IPv4 and IPv6 over same interface between two LSRs while bootstrapping a single LDP session (IPv4 or IPv6)
This violates RFC 5036 which allows any FEC type (unicast IPv4, unicast IPv6, mLDP FEC) over a link regardless of the address family of the Hello adjacency is IPv4 or IPv6.
In RFC 5036, a Hello adjacency over a link is an assertion that a link is associated with the LDP session with the peer, meaning FECs exchanged over the session can be programmed over those links, irrespective of FEC types. Multiple adjacencies on an interface to same peer is violation.
The control of which FEC type is resolved over which interface should be controlled by other means like: LDP capability and/or LDP FEC policies
Notes: <number>

## Slide 3: LDP FEC Resolution with RFC 5036/5283
IETF 84, July 2012
Slide <number>
R1
R2
R3
R4
x (FEC Prefix)
N1
N2
N3
N4
R1 : RIB
…
x -> (1,N1)
(2,N2)
(4,N4)
2
1
3
4
R1: LDP
1. Look-up Peers that advertised address N1, N2, N4 (could be same ipv6 link local). Found peers R2 and R4.
2. Do I have hello adjacencies with R2 on link 1 and 2?
3. Do I have hello adjacency with R4 on link 4?
Route Next-hop = (i/f, nh)
Notes: <number>

## Slide 4: Proposal To Move Forward
IETF 84, July 2012
Slide <number>
We propose to make the following changes to keep FEC resolution compatible with RFC 5036
  Each LSR sends both IPv4 and IPv6 Hello messages over a P2P or Broadcast interface but only a single Hello adjacency must be established on each link to a peer (IPv4 or IPv6)
  User configuration can cause an implementation to send IPv4 only or IPv6 only Hello messages on a P2P interface
  If the single adjacency on the link came up using an IPv4 (IPv6) Hello, it then bootstraps an LDP Session using an IPv4 (IPv6) transport address
The control of which FECs can be resolved to a link can be achieved separately via the support of a new LDP adjacency capability negotiation
  Allows user to configure fate sharing or fate separation in the data path of unicast IPv4 FECs and unicast IPv6 FECs on a link by link basis
  FEC next-hop resolution remains compatible with RFC 5036
  http://www.ietf.org/id/draft-pdutta-mpls-ldp-adj-capability-00.txt
Notes: <number>