## Slide 1
Robert Tao
An Introduction to MPLS-PIM Interworking
(draft-tao-mpls-pim-interworking-00)

## Slide 2
Outline
Problem Overview
An Interworking Approach
Q’s & A’s

## Slide 3
PIM
Site A
Problem Overview
Application Scenario
IP Multicast Sites Around MPLS Backbone
PIM Running In Each Site
PIM Meets MPLS at MPLS-PIM Multicast Border Router (mPMBR)
  PIM Control States
  Multicast Data Traffic
Major Challenges
  Scalability and Performance
  Optimal Routing in MPLS Backbone
  PIM Features
PIM
Site C
mPMBR 1
mPMBR 2
mPMBR 3
MPLS Network
PIM
Site B
P2MP LSP
Recvr2
Recvr1
Src

## Slide 4
Current IETF Approaches And Needs
Approach 1: A 3rd Protocol (i.e. BGP) To Discover and Propagate PIM States (Currently For mVPN)
  RFC6513/RFC6514
  Works with Various Tunnels
Approach 2: Direct State Exchanges between PIM and MPLS
  draft-ietf-mpls-mldp-in-band-signaling-06
  What is missing?
    mLDP Tunnel Only
    Incomplete
      Missing PIM Functions (i.e. ASM)
      No explicit specifications for PIM operations over MPLS (Adjacency, Bootstrapping, RPT to SPT switch)
      No specifications for tunnel aggregations
  What we need: A Framework (Counterpart of RFC6513) To
    Support Various Tunnels
    Complete PIM Features In Efficient and Scalable Ways

## Slide 5
PIM/MPLS Interworking Reference Model
mPMBR
  PIM and MPLS interfaces
  Quasi-PIM Interface (QPI)
    Same as PIM Interface But
    No PIM Adjacency
  PIM-MPLS Interworking (PMIW)
    Mapping PIM Forwarding States
PIM States That Terminate at mPMBRs
  Hello
  Assert
PIM States Mapped Between PIM and MPLS
  PIM Forwarding States
    Per-Interface
    Non-Interface Specific
PIM States Uni-casted Using Raw IP
  Register, CRP-Adv
Bootstrap: A Bootstrap Channel Over MPLS
PIM
Site
Multicast Control Information
IP Multicast data
Note:
PIM
PIM
mFIB
PMIW
mPMBR
MPLS
mLIB
PIM
PIM Interface
MPLS Tunnel
QPI

## Slide 6
Mapping PIM States To/From MPLS States
PIM Upstream
States
Mapping At Leaf mPMBR
M-Flow Spec Data
PIM Per-Interface
States
M-Flow Spec Data
Mapping At Root mPMBR
M-Flow Specs Data
Understood, Consumed By Tunneling Protocols
Bound To P2MP Tunnel
Policy-based Aggregation
Other optimizations within MPLS
PIM States
(*, *, RP)
(*, G)
(S, G)
(S, G, RPT)
Mapping
Propagated and Used
In MPLS

## Slide 7
MPLS-PIM Interworking At Leaf
Suppose There Is A Prospective PIM Upstream State S
MPLS Initiates A Tunnel Signaling with M-Flow Spec(S)
  Skip if it exists for S
Create QPI For The Tunnel
  Skip if it exists
  Bind S to QPI (thus the tunnel)
    Merge M-Flow Spec
Create PIM Upstream state
  QPI as RFP Interface
PIM
MPLS
PMIW
QPI
J/P
S?
PIM Interface
MPLS Interface
Leaf mPMBR Actions
M-Flow
Spec
P2MP Tunnel

## Slide 8
MPLS-PIM Interworking At Root
M-Flow Spec(S) Reaches Root
MPLS Completes Tunnel Signaling
  Skip if it exists for S
Create QPI For The Tunnel
  Skip if it exists
  Bind S to QPI (thus the tunnel)
    Merge M-Flow Spec if necessary
Create PIM Per-Interface State With S
  QPI as RFP Interface
MPLS
PIM
PMIW
QPI
MPLS Interface
PIM Interface
Root mPMBR Actions
Downstream
State
M-Flow Spec(S)
P2MP Tunnel

## Slide 9
PIM Bootstrap Over Backbone
Bootstrap MP2MP Tree
  At Startup, each mPMBR does:
    Designate A Root BSTRAP_ROOT
    Each mPMBR
      Join (BSTRAP_ROOT, ALL_PIM_ROUTERS)
PIM on mPMBR sends and receives Bootstraps
  To/From the channel
  To/From PIM neighbors
BOOTSTRAP
ROOT
BSR1
C-RP(G)
C-RP(G)
Bootstrap
BSR1
…
BSR2
Bootstrap
BSR2
…

## Slide 10
Current State
00 Draft
Initiated Conversations with PIM WG
Next Step
  Acceptance?
  Next Version

## Slide 11
Outline
Problem Overview
An Interworking (In-Band) Approach
Q’s & A’s