## Slide 1: Deep Label Stacks
MPLS part 2, IETF 84
speaker: curtis; voice: kireeti

## Slide 2: Deep Label Stacks
Curtis’s exploration of several forwarding chips led him to think more about the problems that deep label stacks pose to some of the chips
This is to bring the issue to the MPLS WG’s attention, and figure out what (if anything) should be done

## Slide 3: Connection with Entropy Labels
The issue is general, and not related to processing entropy labels per se (or load balancing or …)
However, ELs contribute to deeper stacks
  The entropy label means one more label
  ELI means yet another label
  The idea of inserting multiple ELs in a label stack further increases the depth

## Slide 4: Problem 1: deep label operations
Usually, label operations work with just the top label or two
However, sometimes many labels have to be pushed/popped/swapped
  Reasonable to limit number of labels that can be processed => potentially expensive ASIC resources
  As with many such limits (640K anyone?), time overruns the limit

## Slide 5: PHP vs. UHP
Penultimate hop popping (PHP) is a clever way to distribute deep label operations across several boxes
  However, PHP means that the data plane of an LSP stops short of the control plane
  Theoretical issue: “MPLS architecture is impure”
  Practical issue: “I need stats!”
UHP to get stats means yet more burden to deep label operations: do stats with every pop

## Slide 6: Exceeding Limit #1
What can a chip do if its imposed limit on label depth is exceeded?
  Take a performance hit (lower pps)
  Drop “violating” packets
  Wedge :-)

## Slide 7: Problem 2: Searching for BoS
Even if forwarding decisions require just a few labels, there are times when chips look for the label with the BoS set
This may be to validate the label stack
This may be for load-balancing purposes
  Pick labels near BoS for LB purposes
  Go beyond label stack for fields for LB

## Slide 8: Load Balancing and BoS
From the PoV of load balancing, labels near the BoS are better than labels near the Top of Stack
  think pseudowire labels vs. tunnel labels
Sometimes even this is not enough, and “good” fields for LB come from the payload
  IP fields inside an Ethernet frame in a PW
Fat PW labels and entropy labels obviate the need for this, but these are recent advances

## Slide 9: Exceeding Limit #2
Again, what does a chip do if it doesn’t find a BoS label in its “window of search”?
  Discard packet as “malformed”
  Take a performance hit to search further

## Slide 10: Addressing the Problems
Change chip design to focus on these
  Need guidelines on what to watch out for
Change deployment
  Need “traps” to realize there’s an issue, and knobs to tweak behavior
  Limit stats on a given LSP
Change network architecture
  E.g., add an extra hop to avoid multiple UHPs

## Slide 11: Okay, So What?
Is this a fairly complete list of problems related to depth of stack and BoS?
Survey: who has which problem?
Should the IETF care? MPLS WG? If so, how:
  BCP? For what:
  Chip implementation guidelines?
  Deployment guidelines?
  Network architecture guidelines?

## Slide 12: Next Step
WG chairs + ADs need to tell us whether and how to proceed, starting with how much of this in the IETF scope and in the WG scope
Doing a survey might be helpful to evaluate the depth, urm, extent of the problem
  Logistics may be tricky (NDA, etc.)