## Slide 1: IETF84 A framework for Point-to-Multipoint MPLS-TP OAM in case that return paths don’t exist
draft-hmk-mpls-tp-p2mp-oam-framework.txt
August 3, 2012
Yoshinori Koike Takafumi Hamano
Masatoshi Namiki

## Slide 2: Background
Demand for P2MP traffic is expected to increase due to the increase in new services such as IP-TV and video distribution services.
P2MP is also important in terms of energy efficiency and efficient network resource usage
Agreement in ITU-T to support moving forward p2mp
https://datatracker.ietf.org/liaison/1163/

## Slide 3: Motivation
Inputs to develop MPLS-TP p2mp framework draft(draft-fbb-mpls-tp-p2mp-framework).
As a fast step, focusing on the case of no return path, assuming that OAM is applied on p2mp transport path in conjunction with EMS/NMS

## Slide 4: OAM functional requirements in MPLS-TP (RFC5860)
OAM functions are one of the most important key requirements in transport networks
 | OAM functional requirement | Function | Contents
1 | Continuity Checks | CC | Monitor liveliness of transport path
2 | Connectivity Verifications | CV | Determine whether or not it is connected to specific end point(s) of transport path
3 | Route Tracing | RT | Discover intermediate (if any) and end point(s) along transport path
4 | Diagnostic Tests | DT | Conduct diagnostic tests on transport path (estimating bandwidth, performing loop-back (LB) function of all data and OAM traffic (data-plan LB))
5 | Lock Instruct | LI | Instruct its associated end point(s) to lock transport path
6 | Lock Reporting | LR | Report lock condition from intermediate point to end point of transport path
7 | Alarm Reporting | AR | Report fault or defect condition to end point of transport path
8 | Remote Defect Indication | RDI | Report fault or defect condition to its associated end point
9 | Client Failure Indication | CFI | Propagate information pertaining to client defect or fault condition
10 | Packet Loss Measurement | LM | Quantify packet loss ratio over transport path
11 | Packet Delay Measurement | DM | Quantify delay of transport path (1-way and 2-way)

## Slide 5
A
EMS/NMS
B
C
D
E
F
G
H
J
I
Report from target MEP
First step: in case of no return path
A
B
C
D
E
F
G
H
J
I
Out-of-band return path
First step: Specify requirements, that is necessary information to manage p2mp transport path in case of no return path
In-band OAM packets
1) OAM functions with EMS/NMS
2) OAM functions with return paths to originating MEP

## Slide 6
OAM functions (RFC5860) | Proactive P2MP | On-demand P2MP | Proposed requirements for on-demand P2MP
CC | YES | NA | NA
CV | YES | YES (in case a return path exists) | YES
RT | NO | YES (in case a return path exists) | YES
DT | NO | YES (in case a return path exists) | YES
LI | NO | YES (in case a return path exists) | NO
LR | YES | NA | NA
AR | YES | NA | NA
RDI | YES (in case a return path exists) | NA | NA
CFI | YES | NA | NA
LM | YES | YES | - (Already supported)
DM | YES (only to enable the quantification of the one-way delay) | YES (only to enable the quantification of the one-way delay) | - (Already supported)
Issues on p2mp OAM requirements(RFC5860)
Even if no return path exists, OAM requirements should be achieved in conjunction with EMS/NMS on CV, RT and DT.

## Slide 7
Next steps
Identify what are covered in other RFCs and what are missing as p2mp framework
Specify necessary OAM information/monitored items to be managed at targeting nodes(MEPs) based on the case in which no return path exist
Specify necessary OAM information at source node(MEP) or bud nodes(MIPs) based on the case in which return path exist
Incorporate contents into draft-fbb-mpls-tp-p2mp-framework as needed

## Slide 8
Thank you