## Slide 1: Extensions to RSVP-TE for P2MP LSP Ingress Local Protection
draft-chen-mpls-p2mp-ingress-protection
Huaimo Chen (Huawei)
Ning So (Tata)
Autumn Liu (Ericsson)
Lei Liu (KDDI R&D Lab)

## Slide 2: P2MP LSP Ingress Local Protection
<number>
P2MP
Multicast
Source
Multicast
Receiver
Data
Data
PE1
PE2
PE6
PE5
PE4
PE3
CE4
CE3
CE2
CE1
Main LSP
Backup LSP
Connection for BFD
BFD
-- Locally detect and repair ingress failure
Thus ingress failure recovers within 50ms
1. Ingress PE5 fails
2. Backup ingress PE6 detects it
3. Puts traffic into backup LSP
4. Traffic merged into main LSP
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 3: RSVP-TE Extensions for Ingress Local Protection
<number>
P2MP
PE1
PE2
PE6
PE5
PE4
PE3
Main LSP
Backup LSP
Common Header
LSP Attributes, RRO
LSP Info Msg
Common Header
Protection Flags
Info Conf Msg
1. Ingress PE5 sends LSP Info Msg to backup ingress PE6
4. PE6 sends Info Conf Msg with protection flags to PE5
2. PE6 constructs PATH msg for creating backup LSP
3. PE6 creates FIB entry (inactive) after receiving Resv msg
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 4: Extensions to RSVP-TE for P2MP LSP Egress Local Protection
draft-chen-mpls-p2mp-egress-protection
Huaimo Chen (Huawei)
Ning So (Tata)
Autumn Liu (Ericsson)
Lei Liu (KDDI R&D Lab)

## Slide 5: P2MP LSP Egress Local Protection(Animated)
P2MP
Multicast
Source
Multicast
Receiver
PE1
PE2
PE6
PE5
PE4
PE3
CE4
CE3
CE2
CE1
(S,G)Join
BFD
Data
Data
Main LSP
Backup LSP
-- Locally detect and repair egress failure
Thus egress failure recovers within 50ms
1. Egress PE1 fails
2. PH of PE1 detects it
3. Puts traffic into backup LSP
4. Backup egress PE2 sends traffic to CE1

## Slide 6: RSVP-TE Extensions for Egress Local Protection
. . .
P2MP
PE1
PE2
PE6
PE4
PE3
Main LSP
Backup LSP
PE5
PH of Egress: create backup LSP
Generates PATH msg based on Info and sends along backup path
Creates FIB entry (inactive) for backup LSP after receiving Resv msg
PH of Egress: report status of egress protection
Set node protection bit in RRO for egress when backup LSP is up
Set bandwidth protection bit when backup LSP guarantees to provide the desired bandwidth

## Slide 7: New P2MP LSP E2E Protection
Ingress of P2MP LSP is locally protected (New)
Every egress of P2MP LSP is locally protected (New)
Every link and intermediate node of P2MP LSP is locally protected using FRR (Existing)
Thus
All parts of P2MP LSP are locally protected

## Slide 8: Next Step
draft-chen-mpls-p2mp-egress-protection
draft-chen-mpls-p2mp-ingress-protection
Welcome comments
Request to make it into a working group document

## Slide 9: Advantages of P2MP LSP Ingress and Egress Local Protection + FRR
All parts of P2MP LSP are locally protected
Only one P2MP LSP is used to implement an E2E protection
  Normally two P2MP LSPs are used
Big saving on resource : 50% bandwidth saving
  No need to reserve/use double bandwidth
Faster recovery
  Speed of local protection recovery
  Traffic recovery within 50ms when a failure happens
Easier to operate

## Slide 10: RSVP-TE Extensions for Egress Local Protection
Common Header (Existing)
Label Request (Existing)
Info for Backup Egresses (New)
PATH Message
Sender Descriptor (Existing)
Backup Egress (+Egress)
ERO for backup LSP
Backup Egress (+Egress)
ERO for backup LSP
. . .
Previous Hop (PH) of Egress:
Generates PATH msg based on Info and sends along backup LSP path
Creates FIB entry (inactive) for backup LSP after receiving RESV msg
For one egress to be protected