## Slide 1: Ingress Protection for RSVP-TE p2p and p2mp LSPs draft-torvi-mpls-rsvp-ingress-protection-00
Alia Atlas, Raveendra Torvi, Markus Jork
IETF 84, Vancouver, B.C.

## Slide 2: Basic Problem & Proposed Solution
Problem:
Protect against ingress-node failure for an LSP
Ingress
MP A
Backup
MP B
Egress 1
Egress 2
Traffic Source
Solution:
Proxy-Ingress Node & RSVP Signaling via the Backup Node
  Backup can be on-forwarding-path OR off-forwarding-path
Backup Nodes Uses Bypass Tunnels to reach MPs as in RFC4090.
Ingress
Proxy
Ingress
Backup
MP
Path
Resv
Forwarding

## Slide 3: Failure Detection & Traffic
3 Different Scenarios – signaled in new INGRESS-PROTECTION object
After IGP shows failure, Backup can use make-before-break for global repair.
Detects Failure | Traffic Sent to Backup | Traffic Forwarded From Backup | Traffic Accepted at MP
Traffic Source | On failure | Always | Always
MP | Always | Always | On failure
Backup | Always | On failure | Always

## Slide 4: RSVP Protocol Changes
New INGRESS-PROTECTION object
  Exchanged ONLY from Proxy Ingress to Backup to Ingress (and potentially to MP for MP-detection)
0 1 2 3
+-------------+-------------+-----------------+-------------+
| Length (bytes) | Class-Num | C-Type |
+-------------+-------------+-----------------+-------------+
| Backup Node Address |
+-------------+-------------+-----------------+-------------+
| Ingress Node Address |
+-------------+-------------+-----------------+-------------+
| Application Traffic Identifier |
+-------------+-------------+-----------------+-------------+
| Secondary LSP ID | Protection | Flags |
| | Scenario | |
+-------------+-------------+-----------------+-------------+

## Slide 5: Summary
Simple extension based on proxy-ingress (signaled by ingress) and 1 new RSVP object.
Backup can be on or off the forwarding path.
Backup can use any bypass LSP (p2p or p2mp) for sending traffic as in RFC 4090.
Next Steps
Get feedback on Proposed Solution (on mailing list)
Clarify if any use-cases for reversion back to ingress