## Slide 1: Framework and Requirements for Shared Mesh Protection in MPLS-TP
IETF 84
July, 2012
Yaacov Weingarten
Sam K. Aldrin

## Slide 2: Contributors to SMP
Andrew Malis (Verizon)
Daniel King (Old Dog Consulting)
Eric Osborne (Cisco)
Fei Zhang (ZTE)
Jeong-dong Ryoo (ETRI)
Mohana Singamsetty (Tellabs)
Ping Pan (Infinera)
Yaacov Weingarten
Biao Lu (Infinera)
Dave Allan (Ericsson)
Fatai Zhang (Huawei)
Gregory Mirsky (Ericsson)
Luyuan Fang (Cisco)
Nurit Sprecher (NSN)
Rajan Rao (Infinera)
Sam Aldrin (Huawei)
Tae-sik Cheung (ETRI)

## Slide 3: What is Shared Meshes Protection (SMP)?
The resources on P-Q-R are shared
by multiple working LSP’s
Key properties:
Setup protecting LSP’s ahead of time
All protection related information are pre-computed and loaded to the relevant nodes
Upon failure, use Linear Protection mechanism in switching-over traffic
SMP protocol may be required to coordinate the usage of shared resources
W1
W2
P1
P2

## Slide 4: Background
This is an important function in long-haul transport networks
Multiple parties have been working on it for a long while
There exists several drafts:
  draft-allan-spme-smp-fmwk
  draft-cheung-mpls-tp-mesh-protection-05
  draft-pan-shared-mesh-protection-04
Lack of information to chart a path forward
It’s to everybody’s interest to consolidate

## Slide 5: The Plan @IETF83
Framework and requirements
  (draft-weingarten-mpls-smp-requirements)
SMP Mechanisms and Procedures
  To be published soon

## Slide 6: Update
  Requirement document defines requirements in detail
    Problem definition
    Requirements
    Functional components
    Preemption behavior
    Restrictions
  A common solution, which is within the above framework
  Solution document to be published once WG agrees to the framework and requirements

## Slide 7: SMP Example
Protection
Segment
Protection
Segment
SMP mechanism coordinates the usage of all the shared resources on the protection LSPs
There could be multiple requests contending for same resources
?

## Slide 8: Requirement Highlights
Resource reservation at the time of creation. Actual allocation at the time of activation
Resource coordination while activating and allocation of resources
Ability to query the resource availability
Pre-emption of resources
Priority allocation for primary paths which share protected resources
Notification mechanism
Switch time of 50msec
Hold-Off and Wait-To-Restore timer support

## Slide 9: Summary
Shared Mesh Protection is an important function in TP-enabled transport networks
Received comments. Solicit more comments from WG
Will be publishing new version after incorporating comments