## Slide 1: draft-lzj-mpls-receiver-driven-multicast-rsvp-te-01.txt
Richard Li (renwei.li@huawei.com)
Quintin Zhao (quintin.zhao@huawei.com)
Christian Jacquenet (christian.jacquenet@orange.com)
Receiver-Driven Multicast
Traffic-Engineered Label-Switched Paths
84th IETF @ Vancouver
Notes: <number>

## Slide 2: Quick Review: Receiver-Driven P2MP LSP Setup
At each leaf, one Path message with a downstream-assigned label is sent to its upstream hop
At each branch node, only the first received Path message is sent upstream
For each received Path message, a Resv message is sent downstream
R8
R2
R3
R4
R5
R6
R7
Resv
Path
with Label
Resv
Path
with Label
Path
with Label
Resv
Resv
Path
with Label
Path
with Label
Resv
Path
with Label
Resv
Path
with Label
Resv
R1 (root)
84th IETF @ Vancouver

## Slide 3: Quick Review: Receiver-Driven MP2MP LSP Setup
R8
R2
R3
R4
R5
R6
R7
Resv
With Label
Path
With Label
Resv
with Label
Path
with Label
Path
with Label
Resv
with Label
Resv
with Label
Path
with Label
Path
with Label
Resv
with Label
Path
with Label
Resv
with Label
Path
with Label
Resv
with Label
R1 (root)
At each leaf, one Path message with a label is sent to its upstream hop
At each branch node, only the first received Path message is sent upstream
For each received Path message, a Resv message with a label is sent downstream
84th IETF @ Vancouver

## Slide 4: Questions/Suggestions from 83rd IETF@Paris
Use Cases for MP2MP
  Bootstrap when PIM and MPLS interworking (draft-tao-mpls-pim-interworking)
  MVPN (draft-hlj-l3vpn-mvpn-mrsvp-te)
Split MP2MP and have 2 drafts: RD P2MP and RD MP2MP
  Since the mechanisms to set up MP2MP and P2MP are the same, we thought over it and still prefer to keep them in the same draft
  Any thoughts?
84th IETF @ Vancouver

## Slide 5: Major New and Updated Objects
SESSION
SENDER_TEMPLATE
L2S_SUB_LSP
84th IETF @ Vancouver

## Slide 6: Current Status
Implementation: Close to its completion
Related work:
  FRR: draft-zlj-mpls-mrsvp-te-frr-00.txt
  MVPN: draft-hlj-l3vpn-mvpn-mrsvp-te-00
  Interworking with PIM: draft-tao-mpls-pim-interworking

## Slide 7: Next Steps
Seeking feedbacks from you
Suggestions? Questions? Comments?
84th IETF @ Vancouver