## Slide 1: Quality of Service Option for Proxy Mobile IPv6 draft-ietf-netext-pmip6-qos-00.txt
S. Gundavelli, J. Korhonen, M. Liebsch, P. Seite, H. Yokota
IETF84, Vancouver
NetExt WG
2nd August 2012

## Slide 2: Motivation and Scope
Mobile operator systems enable QoS differentiation to server mobile access through cellular radio
  QoS policy control for 3G radio access from Policy and Charging Control (PCC) system
Connectivity through non-cellular acccess supported for handover (WiFi, WiMax)
  IP network QoS accomplished by DiffServ mechanisms
A single operator deploying both a cellular and a non-cellular access network may want harmonized QoS management
  Standardization started interfacing PCC to MAG for non-cellular radio access
Demand for a PCC-independent solution
  For networks, which do not deploy a PCC system
  For all networks until PCC support available for non-cellular access

## Slide 3: Scope of this work
Support enabling QoS differentiation of traffic between MAG and LMA for any non-cellular access
  In-band QoS signalling, piggybacking PMIP signalling
  Mainly enforcement and validation of uplink QoS at the MAG
Support mapping of QoS policies between radio-specific QoS classes and IP network
  Transport of Flow Information and DSCP
  Implicit mapping detween DSCP and QoS Class Indexes
  Interpretation of QoS information is deployment specific, hence out of scope
Focus on the signaling between MAG and LMA
Handover of available and enforced QoS policy rules
  Established while MN accesses through 3G radio access
Establish QoS for sessions which start at non-3G radio access

## Slide 4: Status
Initial version of this draft presented at IETF82 in Taipei
Adopted as WG document after IETF83 in Paris
  Received valuable comments during last call
    Editorial fixes in -00
    Implicit mapping between DSCP and QoS Class Indexes
      E.g. according to GSMA/3GPP mapping for EPC/LTE
  Update required to clarify applicability of the QoS information
  Can apply at the MN scope,
  Or per-mobility session,
  Or on a per flow basis.

## Slide 5: QoS option
New option for PBU/PBA
  MN scoped option or applies either at the mobility session or at the IP flow level

## Slide 6: Optional QoS Information (sub-options)
So far described in the specification:
Per MN Aggregate Maximum Downlink Bitrate
Per MN Aggregate Maximum Uplink Bitrate
Per Mobility Session Aggregate Maximum Downlink Bitrate
Per Mobility Session Aggregate Maximum Uplink Bitrate
Allocation and Retention Priority (ARP)
Guaranteed Downlink Bitrate
Guaranteed Uplink Bitrate

## Slide 7: To be discussed
Do we need a vendor specific option?
  E.g. to be flexible in the definition of QoS information
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Vendor ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sub-Type | Data.......
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 8: Main Use Cases
Handover of established QoS rules to non-cellular radio access
  Apply same QoS differentiation on the path between LMA and MAG, which serves
  Enable mapping of admitted QoS classes to QoS differentiation techniques of non-cellular access, e.g. .11e
Estabblishment of QoS rules while MN is attached to non-cellular radio access
  MAG may propsose QoS rules to LMA for approval
    Priority class indicated in uplink
    MAG may assess QoS according to flow information
    MN may utilize access-specific control plane (e.g. WMM) to indicate demand for QoS differentiation
  LMA authorizes proposed QoS or assesses QoS according to flow information

## Slide 9: Operation: Handover of QoS rules

## Slide 10: Operation: Establishment of QoS rules