## Slide 1: Network Mobility with Proxy Mobile IPv6 draft-petrescu-netext-pmip-nemo-01
Alexandru Petrescu (speaker),
Michael BOC,
and Christophe Janneteau
IETF 84, Vancouver, August 2nd, 2012

## Slide 2: Problem of Network Mobility
Problem of network mobility in a PMIP domain:
  PMIP allocates a /64 prefix HNP to a Mobile Host
  HNP topological correctness only on MH-MAG iface
  HNP connected route on MAG
  LFNs need addresses
  MAG would need a classical non-connected route for parts of HNP, towards MH interface
Need allocation of a MNP (Moving Network Prefix) to a MR

## Slide 3: PMIP Network Mobility problem
A3
MAG1
MAG2
LMA
MR
(handover)
LFN1
Towards Internet
MAG1
MAG2
LMA
MH
(handover)
Towards Internet
A1; LLMH@
Routing Table
[HNP, LLMH@]
Routing Table
[HNP, LLMR@]
[MNP, LLMR@]
LLMR@
A1;
Routing Table
[HNP, egress]
[A1, egress]
Routing Table
[A1, egress]
[MNP, ingress]
A5
A6
PMIP HNP, with MH
Need MNP for LFNs
Moving Network
PMIP Fixed
Infrastructure
LFN1
MNP needed!

## Slide 4: Design Considerations of Delegating a Prefix in a PMIP context
Should MNP be allocated by whom?
  DHCP?
  PMIP?
  Derived from HNP?
Should LMA allocate a prefix?
  or should it accept a prefix allocated by DHCP?
Should have support for shared links?
  or for ptp links?
Should LMA be co-localized with a DHCP Server?
  or should it be separated?
« Proxy »
  should use proxy Neighbor Discovery on MR?
  should use proxy DHCP on MR? On MAG? On LMA?
  or should avoid use of proxies and bridges?
How to auto-configure LFNs out of MNP?
  will /65 work with SLAAC and LFNs?

## Slide 5: PMIPv6-NEMO with DHCPv6-PD (1/2)
Extension of I-D PD-PMIP?
What’s different?
  Prefix delegation ensured by DHCPv6-PD (vs. ensured by LMA)
    Hints supported
    Multiple PDs in request supported (vs. only a single one, PBU MNP=0)
  Mobility mgmt of delegated prefixes ensured by PMIPv6
    Prefixes are imposed by DR to LMA (vs. imposed by LMA to DR)
  DHCP DelgRtr can be separated from LMA (vs. DR MUST be co-located with LMA)
  MAG changes DHCPv6’s DUID to PMIPv6’s MNID
    MNID is a common identifier between PMIP and DHCP databases (vs. no link betwen DR and LMA’s databases)
  Bit Q (vs. Bit R)
  Lifetime management is necessary (vs. permanent)

## Slide 6: PMIPv6-NEMO with DHCPv6-PD (2/2)
DHCP relay-reply
(MNID,MNP/Y)
DHCP Relay-forward
(DUID=MNID, MNP/X)
MR
(Requ.Router)
DHCPv6 Relay
MAG
LMA
DHCPv6 Server
(Delegating Router)
LFN
CN
Data using
HNP & MNP
Tunnel IPv6-in-IPv6
RA(MR=Default router)
MR is registered at LMA (PMIPv6 normal procedure) and has HNP(s)
DHCP Reply
(DUID,MNP/Y)
RA(MNP/64) or
DHCPv6(MNP/128)
PBU (MNID, MNP/Y)
PBA (MNID, MNP/Y)
DHCP Request (DUID,MNP/X)
Delegating router
may not be co-located
with LMA
Provided IA PD hint
may be considered
DUID is changed
to PMIPv6’s MNID
PMIPv6’s MNID is
changed back to DUID

## Slide 7: PMIP Network Mobility, HNP Division
Could be an extension to PMIP:
  PBU tells LMA that a MNP is out of HNP
Self-form MNP out of HNP (alternative to use DHCP-PD )
Offer network mobility, without modification of PMIP messages
Works on ptp links, not on shared links

## Slide 8
A 11000
A1 11001
A2 11010
A3 11011
A4 11100
A5 11101
A6 11110
A7 11111
A0 11000
HNP /2
MNP1 /4
MNP2 /3
HNP Division
To be used by LFNs
To be used by MR’s egress
To be used by LFNs
Example HNP division with hypothetical
5bit addresses
HNP/2  A/5, MNP1/4
and MNP2/3
HNP/64  A/128, MNP1/66 and MNP2/65.

## Slide 9
Similar Prefix Division concepts alluded to in:
  draft-krishnan-intarea-pd-epc-00, « Prefix Delegation in EPC Networks », 2010.
  draft-arkko-homenet-prefix-assignment-01, « Prefix Assignment in a Home Network », 2011.
There is implementation of PMIP-NEMO

## Slide 10
Questions to the group:
  Is HNP Division an attractive way of creating MNP
  Is separation of DHCP Server from LMA good for deployments