## Slide 1: Behcet Sarikaya Frank Xia July 2012
Flow Binding Extensions to PMIPv6 IETF 84
draft-sarikaya-netext-fb-support-extensions-02

## Slide 2: Problem Statement
  LMA initiated flow mobility is not possible in PMIPv6 of RFC 5213
  PMIPv6 Multihoming extension (RFC 5213) treats each interface independently
  LMA does not know about different interfaces MN may have, LMA does not manage bindings from different interfaces of the mobile node in an integrated fashion
  Each interface creates a different independent mobility session at the LMA, just like an interface from another MN
  MN uses different source addresses when sending packets over these interfaces
  Flow mobility is not possible

## Slide 3: draft-sarikaya-netext-fb-support-extensions
We have a simple solution:
The bindings in binding cache from each interface are kept together so that the flows can be moved among interfaces.
MN may have as many binding entries as it has active interfaces, one “home” and many “secondary”, flagged “H” or “S”
A new H flag in HNP option is set to ‘H’ for home and ‘S’ for other interfaces
Incoming flows always directed to home interface, flow state set at LMA to direct flows to different active interfaces
MN always sends non-local packets with source address assigned from HNPs of its home “H” interface

## Slide 4: draft-sarikaya-netext-pmipv6-shared-link-01
Wi-Fi or IEEE 802.11 provides a shared link
PMIPv6 is designed for point-to-point links, i.e. cellular links
Why do we need to run PMIPv6 on Wi-Fi?
The answer is SaMOG or s2a interface for FMC
Issues: MAG sends RA with HNPs for MN to FF02::1 which could be received by other MNs
  serious
MN may receive NS messages from nodes other than MAG due to IPv6 solicited-node multicast address may map to more than one nodes
  Less probable
Multicast data using MLD: problems TBD