## Slide 1: Network Virtualization Overlays Use Cases draft-timy-nvo3-use-case-01
Lucy Yong Mehmet Toy
Aldrin Isaac Vishwas Manral
Linda Dunbar
Vancouver July 31, 2012

## Slide 2: Network Virtualization Overlays Promise
Compute system and physical networking decoupled
  Both systems and networking exist in a virtual environment
Virtual networks are built on a common infrastructure with:
  Traffic isolation among one another, independent address space in each
  VM placement and move from one server to another without physical network limitation
VM
VM
VM
VM
VM
VM
VN1
VN2
VN3
Virtual
VM
VM
VM
VM
VM
VM
Physical
vSwitch
vSwitch
vSwitch

## Slide 3: NVO3 Use Cases
I. Virtual Networks in One Data Center
  Provide communications among the VMs in a closed use group
  Use for DC internal applications
II. Interconnection between DC virtual network and external user
  One virtual network method in DC and WAN
  VN and VPN interconnection at DC Gateway
  Connecting a DC virtual network via Internet
VM
VM
VM
VM
VM
VM
VN1
VN2
VN3
VM
DC
WAN
GW
VPN
Internet
GW
VM
VM
DC1
DC2
(1)
(2)
(3)

## Slide 4: NVO3 Use Cases Cont’
III. DC applications using virtual networks
  Multi virtual networks to interconnect a large amount of VMs in DCs
    Individual VNs may be L2 or L3
    May contain multiple topologies
    Gateway interconnect VNs
  Virtual Data Center
    Network services per virtual network
    Client manages applications running in vDC
    DC operators manage vDC
Details are illustrated and described in the draft
VM
VM
L2VN
VM
VM
L2VN
L3VN
DC1
DC2
DC
WAN
GW
GW
VM
VM
VM
Internet
Firewall/Security
Monitoring
Load Balancer
Bridging/routing
Network Service:
vDC
GW

## Slide 5: NVO3 Applicability
NVO3 differs from traditional overlay technologies in
  A virtual network connects to and is aware of VMs
  Virtual network edge and VMs resides on the same hardware
  VN and VM are managed by the same orchestration
NVO3 brings the ability of building IT applications in a true virtual environment
  Construct IT applications without worry about physical network limitations, enable IT new applications
  Speed up in building vDC, private or public cloud applications for various customers
NVO3 has to address how to communicate between a virtual environment to a physical environment
  Many traditional DCs exist today and not disappear soon
  A large of DC applications serve to Internet or corporation users

## Slide 6: Next Step
Welcome comments and suggestions
Authors request adopting the draft as WG draft