## Slide 1: OSPF Stub Router Advertisement (draft-ietf-ospf-rfc3137bis-02)
Alvaro Retana, Liem Nguyen, Russ White, Alex Zinin, Danny McPherson
alvaro.retana@hp.com, {lhnguyen, azinin}@cisco.com, {riwhite, dmcpherson}@verisign.com

## Slide 2: What is RFC3137?
OSPF Stub Router Advertisement
  Category: Informational
  Publication: June 2001
Describes a backward-compatible technique that may be used by OSPF to advertise unavailability to forward transit traffic (rfc1247) or to lower the preference level for the paths (rfc1583) through such a router.
  Solution: the costs of all non-stub links are set to MaxLinkMetric

## Slide 3: Update
Explicitly added support for OSPFv3.
  Generalized text to avoid OSPFv2-specific references.
  Referenced existing OSPFv3-only solution (R-bit)
Defined a new architectural constant (MaxLinkMetric) to eliminate any confusion about the interpretation of LSInfinity.
  MaxLinkMetric
  The metric value indicating that the link described by an LSA
  should not be used as transit. Used in router-LSAs (see
  Section 3). It is defined to be the 16-bit binary value of all
  ones: 0xffff.

## Slide 4: Next Steps
Request WGLC and Publication
  Category: Informational