## Slide 1: OSPF Topology-Transparent Zone
Huaimo Chen, Renwei Li (Huawei)
Gregory Cauchie (France Telecom)
Ning So (Tata)
Lei Liu (KDDI R&D Lab)
Alvaro Retana (HP)

## Slide 2
Page <number>
Contents
Some changes/options for TTZ
Requirements for TTZ
Introduction
Next Step
Notes: <number>

## Slide 3: Definition of TTZ
A group of routers connected by links with TTZ ID
  which is virtualized as
    a group of TTZ edge routers fully connected or a single router
  of which routers outside TTZ are NOT aware
  through which LSAs outside are distributed
Links, routers inside TTZ are NOT advertised to routers outside of TTZ
R6
R8
R10
R2
R3
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ
T4
T3
T10
T1
R6
R8
R10
R2
R11
R3
R5
RT
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ
Focus on
A group of TTZ edge routers
A single router

## Slide 4
Page <number>
Contents
Some changes/options for TTZ
Requirements for TTZ
Introduction
Next Step
Notes: <number>

## Slide 5: Requirements for TTZ
TTZ MUST support 1+ levels of network hierarchies
TTZ MUST be backward compatible
Users SHOULD be able to easily set up an E2E service crossing TTZs
Configuration for a TTZ SHOULD be minimum
Changes on existing protocols SHOULD be minimum
Page <number>
One more hierarchies
Area 0
Area 1
TTZ
TTZ
TTZ
TTZ
TTZ
Area 0
Area 2
Area 3
Area 4

## Slide 6
Page <number>
Contents
Some changes/options for TTZ
Requirements for TTZ
Introduction
Next Step
LSA Change
Adjacency Establishment
Changes/Options for TTZ as a single router
Notes: <number>

## Slide 7: LSA Change — I bit
Page <number>
1 bit to identify if a link is in TTZ
0
1
2
7
I
Link Type
I = 1: Link is in TTZ
I = 0: Link is not in TTZ
Meaning of “Link Type” of 7 bits is the same as that of “Link Type” of 8 bits.
0
1
2
7
Link Type
Options
LS Age
Link State ID
LS Sequence Number
LS Checksum
Advertising Router
Length
Number of Links
I bit = 1 if link in TTZ
LS Type = 1
Router Link
Router Link
. . . . . .
Flags
Header
I bit = 1 if
link in TTZ
Router LSA

## Slide 8: Adjacency (to non TTZ) Establishment
Between TTZ edge and non TTZ router, TTZ edge
  sends non TTZ router hellos in a normal way, and
  sends non TTZ router all the LSAs except for the LSAs belong to TTZ during LSDB synchronization.
After adjacency is established, TTZ edge router
  floods the LSA that does not belong to TTZ to the non TTZ router through the adjacency
Page <number>
R6
R7
R8
R10
R9
R4
R1
R2
R11
R3
R5
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ

## Slide 9: Adjacency (to TTZ) Establishment
Options:
In the same way as a normal router
Hello is extended to include TTZ ID in hello packets
  When two routers have the same TTZ IDs in their hellos, an adjacency between them is to be formed.
Page <number>
R6
R7
R8
R10
R9
R4
R1
R2
R11
R3
R5
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ

## Slide 10
Page <number>
Contents
Some changes/options for TTZ
Requirements for TTZ
Introduction
Next Step
LSA Change
Adjacency Establishment
Changes/Options for TTZ as a single router
Notes: <number>

## Slide 11: Adjacency (to non TTZ) Establishment -- TTZ as a single router
Between TTZ edge and non TTZ router, TTZ edge
  sends non TTZ router hellos in a normal way but with RT ID, and
  sends non TTZ router all the LSAs except for the LSAs belong to TTZ during LSDB synchronization.
After adjacency is established, TTZ edge router
  floods the LSA that does not belong to TTZ to the non TTZ router through the adjacency
Page <number>
R6
R7
R8
R10
R9
R4
R1
R2
R11
R3
R5
RT

## Slide 12: Router ID of a single router for TTZ
RT ID: Largest or smallest interface IP address of TTZ-DR
  Used in hellos sent to non TTZ router from TTZ edge router
  Used in LSA (LS ID and Advertising Router) for the router for TTZ
RT ID: TTZ ID
Page <number>
R6
R7
r8
R10
R9
R4
R1
R2
R11
R3
R5
RT
Normal Link
Normal Link
Normal Link
Options
LS Age
Link State ID (RT)
LS Sequence Number
LS Checksum
Advertising Router (RT)
Length
Number of Links
LS Type = 1
Router Link: RT to R2
Router Link: RT to R11
Flags
Header
Router Link: RT to R3
Router Link: RT to R10
. . .

## Slide 13: Next Step
Welcome comments

## Slide 14: LSA Generation and Flooding
Every router in TTZ generates a router LSA containing all the router links, each of which has I bit set to 1 if it is configured with TTZ ID. This LSA is flooded inside TTZ.
TTZ virtualized as
  A group of routers connected: TTZ edge router constructs a second router LSA and sends it to all its neighbors. This LSA comprises two groups of links.
    The router links connecting the routers outside of the TTZ from this TTZ edge router. These router links are normal router links. There is a router link for every adjacency between this TTZ edge router and a router outside of the TTZ.
    The "virtual" router links. For each of the other TTZ edge routers, there is a "virtual" router link to it from this TTZ edge router. The cost of the router link from this TTZ router to one of the other TTZ edge routers is the cost of the shortest path from this TTZ edge router to it.
  A single router: DR of TTZ constructs a second router LSA and sends it to all its neighbors. This LSA comprises links between a TTZ edge router and a router outside of TTZ.
Page <number>

## Slide 15: Router LSA Generated by T1/T5 to inside TTZ
R6
R7
R8
R10
R9
R4
R1
R2
R11
R3
R5
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ
Options
LS Age
Link State ID (T1)
LS Sequence Number
LS Checksum
Advertising Router (T1)
Length
Number of Links
I=0 for Normal Link
LS Type = 1
Router Link: T1 to R2
Router Link: T1 to T5
Flags
Header
Router Link: T1 to T2
Router Link: T1 to T4
I=1 for TTZ link
I=1 for TTZ link
I=1 for TTZ link
Options
LS Age
Link State ID (T5)
LS Sequence Number
LS Checksum
Advertising Router (T5)
Length
Number of Links
I=1 for TTZ Link
LS Type = 1
Router Link: T5 to T1
Router Link: T5 to T9
Flags
Header
Router Link: T5 to T4
Router Link: T5 to T6
I=1 for TTZ link
I=1 for TTZ link
I=1 for TTZ link

## Slide 16: Router LSA by T1 to outside TTZ as a Group of Nodes Connected
Page <number>
R6
R7
R8
R10
R9
R4
R1
R2
R11
R3
R5
T4
T3
T10
T1
Options
LS Age
Link State ID (T1)
LS Sequence Number
LS Checksum
Advertising Router (T1)
Length
Number of Links
Normal Link
LS Type = 1
Router Link: T1 to R2
Router Link: T1 to T10
Flags
Header
Router Link: T1 to T3
Router Link: T1 to T4
Normal Link (“virtual”)
Normal Link (“virtual”)