## Slide 1: draft-ospf-non-compatible
Mike Dubrovsky

## Slide 2: The draft addresses the following problem:
Problem:
How to introduce non-backward compatible functionality into ospf protocol
The solution is simple:
Turn on the functionality only when all participating routers support it.
… But we need a signaling method.

## Slide 3: Current ospf standard
OSPF historically uses Options Field for non-backward compatible changes
In ospfv2 we run out of bits (8 total, 0 free)
In ospfv3 we still have plenty of bits (24 total, about 16 free)
For AS-wide functionality the Indication-LSA is used.

## Slide 4: Current ospf standard: RI LSA
Router Information LSA overcomes the Options Filed bits unavailability problem in ospfv2 by introducing a TLV based solution. It also removes the restriction on a number of bits for ospfv3.

## Slide 5: Current ospf standard: RI LSA
Router Information LSA packet format
ospfv2
Opaque LSA
New opaque Type # 4
ospfv3
New LSA code 12
RI TLV with a variable length bits string
…..
Other TLVs

## Slide 6: Conclusion on current ospf standard
Ospfv2 does not have a standard mechanism
to introduce new AS-wide functionality
Ospfv3 still has about 16 bits for new enhancements and can reuse the existing Indication-LSA for domain wide functionality

## Slide 7: Proposed Solution
Generalization of demand circuit mechanism
using the RI LSA based approach.
Use Router Information LSA for link and area wide functionality
To signal across area boundaries in the case of AS-wide functionality, we adopt a solution similar to the Indication-LSA but based on TLV.

## Slide 8: Proposed Solution: AI LSA
Area Information LSA packet format
ospfv2
Opaque LSA
New opaque Type # TBD
ospfv3
New LSA code TBD
AI TLV with variable length bits string
…..
Other TLVs

## Slide 9: Proposed Solution Examples
3 examples of new functionality
Sync RFC1583Compatibility parameter
Sync ospfReferenceBandwidth parameter
Sync extended metric

## Slide 10: ospfReferenceBandwidth Synchronization
A router with the highest ospfReferenceBandwidth sends the advertisement across the AS.
Same RI/AI LSAs are used to propagate the ospfReferenceBandwidth in a separate TLV.

## Slide 11: Points of compromise
Do we need to standardize AS-wide non-compatible extension for ospfv2
(we don’t have too often a new extension) ?
2) Should we use a separate AI LSA or
add TLV to RI LSA
3) Do we need any of these 3 proposed extensions ?
4) Where to put reference-bandwidth value advertisement
(RI LSA is fine – but a little bit of stretch)?

## Slide 12: Q & A
Questions ?
Answers ?