## Slide 1: PAWS WG IETF-84
Device to Database Protocol for White Space
<draft-das-paws-protocol-02.txt>
July, 2012
Subir Das, John Malyar, Don Joslyn

## Slide 2: Protocol Layer
+-+-+-+-+-+-+-+-+-+-+-+-+
| PAWS | +-+-+-+-+-+-+-+-+-+-+-+-+
| HTTPS |
+-+-+-+-+-+-+-+-+-+-+-+-+
| TCP/IP |
+-+-+-+-+-+-+-+-+-+-+-+-+
| IP |
+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 3: Protocol Features/Functionalities
WSD Initialization
WSD Registration
Database Query and Response
Channel use Notification and Response
WSD Validation
WSD = White Space Device

## Slide 4: Mailing List Discussion Points and Issues
Purpose of WSD Initialization
Purpose of WSD Registration
Device Authentication
Data Model
  Lat/Long representation
    Use of separate ‘geolocation’ , ‘civiclocation’ elements
  Use if ‘vCard’ for ‘deviceowner’ data element
  Use of ‘iCalendar’ for channel availability time

## Slide 5: WSD Initialization
Assumption
  WSD Knows the URI of the DB or the discovery service
  WSD establishes HTTPS connection with the DB
    Server certificate is authenticated against a well known certificate authority
WSD initialization is performed using INT-REQ and INT-RESP messages . The purpose of this step are two folds:
  To perform the Client authentication using a shared secret ( by using Digest Authentication)
    ‘Authinformation’ data element is used for this purpose
  To exchange several authority/domain specific information which are not possible to obtain during DB discovery, e.g.,
    Device type, Serial number, Regulatory id, frequency when Master WSD should query the database, Result code and so on
      ‘Capabilityinfo’ and ‘Protocolinfo’ data elements are used for this purpose

## Slide 6: WSD Registration
WSD registration is performed using REG-REQ and REG-RESP messages. The purpose of this step is:
  Provide the database with operational parameters such as owner and/or operator contact information, location and antenna height parameters and so on
    ‘Devicelocation’ , and ‘Deviceowner’ data elements are used for this purpose
This step may be required by some spectrum management authorities
  Registration can be mandatory upon its initial contact with the database, or when its registered parameters change

## Slide 7: Device Authentication
We believe that device authentication should be done by using a shared secret model instead of a client certificate and we provide the following:
  The use of Digest Authentication is identical to that for HTTP [RFC2617] and in particular SIP [RFC3261] with the following modifications:
    The URI and method included in the challenge are empty
    The realm represents one ‘security realm‘
    The device’s serial number is currently mapped to ‘username‘ and the device’s shared secret is mapped to ‘password‘
    MD5 is replaced by SHA-1

## Slide 8: Data Model: Example
Draft currently specifies the simple data elements for device location and device owner (light weight and self contained)
    Device Location:
      Latitude ; type=float
      longitude ; type=float
      Locuncertainty; type==number
      Locconfidence; type=number
      HAGL; type=number
      HAGLuncertainty; type=float
      Antennatype; type= int
    Device Owner:
    Ownername; type=string
    Address ; type=string
    Phonenumber; type=alphanumeric
    Email; type=alphanumeric
Using the structure as specified in RFC 5491 and RFC 5139 may be fine but we have concerns over future compatibility (e.g., recent open geospatial name space change seehttp://www.ogcnetwork.net/node/1829)

## Slide 9: Use of vCard and ical
Our understanding is that PAWS requirements would use less than 20% of the properties defined in vCard and iCal
PAWS Requirements related to vCard use are
  Name;
  postal address;
  email address ; and
  phone number;
PAWS Requirements related to ical use are
  Duration; and
  Time ;
Can we simply use the following from iCalendar (RFC 5545)?
  DTSTART , DTEND / DURATION

## Slide 10: Message Encoding with JSON: Example
AVAIL-CHAN-REQ
  POST/AVAIL-CHAN-REQ HTTPS/1.1
  Host:WSP.example.com:443
  Content-Type:application/PAWS+json; charset=utf-8
  content length: XX
  {
  "Protoversion": "1.0",
  "messagetype": "AVAIL_CHAN_REQ",
  "Authority": "US",
  "Devicetype": "F",
  "Deviceidentity": "TTT1234",
  "Deviceserialno": "01AB23CD45EF",
  "Latttitude": "40.5414",
  "Longitude": "-74.4750"
  "Locuncertainty": "2",
  "LocConfidence": "95",
  "HAGL: " 25",
  "HAGLuncertainty": "1",
  "Antennatype":"MM",
  "Geolocationcode":"DEFAULT",
  "Requesttype":"allchannels",
  "Authscheme": "DIGEST",
  "Realm":"PAWS-DDI",
  "Nonce": "7b52009b64fd0a2a49e6d8a939753077792b0554"
  "Cnonce":"bd307a3ec329e10a2cff8fb87480823da114f8f4",
  "qop": "auth"
  "resp": "4dfb972d427b4100c821d53b8bea9b2c33b74a7e",
  }
AVAIL-CHAN-RESP
POST/AVAIL-CHAN-RESP HTTPS/1.1 200 OK
Server: Example PAWS
Date: Fri, 12 June 2012 06:24:27 GMT
Expires: Fri, 12 June, June 2012, 20:30:00, GMT
Cache-control : private
Content-Type:application/PAWS+json; charset=utf-8
content length: YY
{
"Protoversion": "1.0",
"Messagetype": "AVAIL_CHAN_RESP",
"Authority": "US",
"Resultcode": "success", "Authscheme": "DIGEST",
"Realm":"PAWS-DDI
"Nonce": "7b52009b64fd0a2a49e6d8a939753077792b0554"}
"qop": "auth",
"Channellist": [
{ "Channelno": 2,
"Minfreq": 54,
"Maxfreq": 60
"MaxEIRP": 4000,
"Datetime": "20120612T235959Z",
"Duration": "1440, mins",
"Availability": true.
.
.
{
"Channelno": 51,
"Minfreq": 692,
"Maxfreq": 698,
"MaxEIRP": 4000,
"Datetime": "20120612T120000Z",
"Duration": "720, mins ",
"Availability": true
}

## Slide 11: Next Steps/Considerations
We have received comments from several folks (Thanks to the reviewers!) such as,
  ‘Channel number’ should be optional and frequency should be mandatory
  Device authentication should be optional
    Device authentication may be performed by using cert where available
  Regulator specific attributes should be listed or profiled in the Appendix
  ‘Device owner/operatorinfo’ may be represented using ‘vcard’
  ‘Channel/Frequency’ availability may be represented using ‘ical’
Our goal is to discuss further and address them as appropriate in our next version

## Slide 12
Questions? Feedback?

## Slide 13: Backup Slides

## Slide 14: DB Query
Database query and response are performed using AVAIL-CHAN-REQ, and AVAIL-CHAN-RESP messages. The purpose of the step is
  To query the WS database with the required parameters for obtaining WS channel/frequency information
    ‘Devicelocation’, and ‘Availablechannellist’ , data elements are used for this purpose
Used channel/frequency notification and response are performed using USE-CHAN-NOTIFY and USE-CHAN-RESP messages. The purpose of this step is,
  To notify the used channel/frequency information to the database
    ‘Devicelocation’, and ‘Usedchannellist’ data elements are used for this purpose

## Slide 15: WSD Validation
WSD validation is performed by using DEV-VALID-REQ and DEV-VALID-RESP messages. The purpose of this step is
  Master WSD verifies the identity of the slave WSDs when required by the spectrum management authority
    ‘Devicelocation’ and ‘Slavedevicelist’ data elements are used for this purpose

## Slide 16: Data Model Structure
Object
Element
Attribute
Initialization
Registration
DatabaseQuery
Devicevalidation
Capabilityinfo
Protocolinfo
Authenticationinfo
Deviceowner
Availablechannellist
Devicelocation
Usedchannellist
Slavedevicelist
Devicetype
Deviceidentity
Lattitude/Longitude
Max/Min Freq
HAGL
MaxEIRP
.
.
.
.
MaxEIRP