## Slide 1: PCEP MIB – an update
AS Koushik
Stephan Emile
Quintin Zhao
Daniel King
Jon Hardwick (presenting)
draft-ietf-pce-pcep-mib-03

## Slide 2
Summary of changes from -02 to -03
Terminology change pcePcepClient -> pcePcepEntity
Session table no longer augments peer table
Various fields added to be in line with RFC 5440
Various fields retired
  See mailing list for details

## Slide 3
Next steps
PCEP MIB
  More statistics – what would be most useful?
  Performance and congestion metrics
  Further configuration is possible if we want to standardize it
    Permissions and access policies
    Path computation capabilities
    Session establishment policies
    ...
PCE Discovery MIB
  Revive this after the current meeting
PCE Textual Conventions
  Is there still a need for this?

## Slide 5
Backup – removed fields I
pcePcepClientSessionAuth
This was incomplete as specified and might best be left to the implementation. For example, the setting onlyAuthorizedPeers is not meaningful without some way to configure the authorized peers.
pcePcepClientStorageType
Again this is probably best left to the implementation.
pcePcepClientInitSession
This was incomplete as specified and might best be left to the implementation. It only allows “automatically connect to everyone” and “do not connect to anyone”. There are many different policies that you might wish to apply between those two extremes.
pcePcepClientPoliciesAllowed
This was incomplete as specified and might best be left to the implementation. Has an exhaustive list of path computation policies been standardized anywhere?

## Slide 6
Backup – removed fields II
pcePcepPeerLastChange
This is covered adequately by the new time values within the peer and session MIBs.
pcePcepSessionDiscontinuityTime
This is covered adequately by the new time values within the peer MIB.
pcePcepSessionSpeakerRole
This was structurally wrong. A role is a property of an individual request, not an entire session.
pcePcepSessionCorruptedMsgs
We need a tighter definition in the MIB of what is “corrupted” versus “unsupported” and it might be better to count them separately. For example, if an object type is not recognized, how do you know whether the message was corrupted?
pcePcepSessionFailedComps
There are different categories of failure and it might be better to split them out: NO-PATH; undecipherable request; policy rejects request; and so on.