## Slide 1: Extensions to Path Computation Element Communication Protocol (PCEP) for Hierarchical Path Computation Elements (PCE)
PCE WG, IETF 84
draft-zhang-pce-hierarchy-extensions-02
F. Zhang (Huawei)
Q. Zhao (Huawei)
O. González de Dios (Telefonica I+D)
R. Casellas (CTTC)
D. King(Old Dog Consulting)
Notes: <number>

## Slide 2: Differences from 01
Editorial points :
  Changed to XML format
  Corrected some typos and wording
Requirements section:
  Some subsections were redundant in -01 version.
  Some subsections have been merged and aligned with the requirements draft
  Added “Determination of destination domain” to align with the framework draft
Align OF to those on the framework
Added New Metrics: Domain Count and BN count.
Added a Reachabilily TLV.
Notes: <number>

## Slide 3: New OF
Alignment of new OF to those on the framework
  Minimize or cap the number of domains crossed
  Disallow domain re-entry
New OF: Minimize number of domains
Cap the number of domains can be viewed as a limit in a metric (e.g. number of domains)
We think disallow domain re-entry is a policy
Notes: <number>

## Slide 4: New metric
Framework document mentions the need to cap the number of domains crossed
Proposal: add new metric with number of domains crossed
Proposal: add new metric with number of BN (to differentiate between cases with one BN common to two domains, and cases with inter-domain links)
Notes: <number>

## Slide 5: Reachabilily TLV
The reachability TLV carries information of the set of end-points reachable in a given domain.
The format of the TLV is a list of IPv4 Prefix, IPv6 Prefix, AS and unnumbered Interface ERO subojects, as defined in [RFC3209] and [RFC3477].
This TLV can be carried in a NOTIFICATION object to indicate the reachable end-points of the domain of the PCE who sends the PCNtf message.
Notes: <number>

## Slide 6: Next Steps
Receive feedback!
The framework document for H-PCE is almost ready.
This solution document could be a base for a WG document for the solution of the framework.
Notes: <number>

## Slide 7
Questions?