## Slide 1
Bisong Tao Huawei Technologies Inc.
An Introduction to MPLS-PIM Interworking
(draft-tao-mpls-pim-interworking-00)
Notes: <number>

## Slide 2
Outline
Problem Overview
An Interworking Approach
Q’s & A’s
Notes: <number>

## Slide 3
PIM
Site A
Problem Overview
Application Scenario
IP Multicast Sites Around MPLS Backbone
PIM Running In Each Site
PIM Meets MPLS at MPLS PIM Border Router (mPMBR)
  PIM Control Traffic
  Multicast Data Traffic
Challenges
  Scalability and Performance
  Routing in MPLS
  PIM Features
PIM
Site C
mPMBR 1
mPMBR 2
mPMBR 3
MPLS Network
PIM
Site B
P2MP LSP
IP Multicast
Notes: <number>

## Slide 4
Problem Overview
Current Solutions
Out-Of-Band Method For mVPN
  RFC6513, RFC6514
  RFC6037(Cisco)
  draft-hlj-l3vpn-mvpn-mrsvp-te-00
In-Band Method For mLDP
  draft-ietf-mpls-mldp-in-band-signaling-06
Problems
Dependence on A Third Protocol
Incomplete PIM support
Performance and Scalability
  Overheads Caused to Backbone
  Optimal Routing in Backbone
Notes: <number>

## Slide 5
Outline
Problem Overview
An Interworking Approach
Q’s & A’s
Notes: <number>

## Slide 6
PIM/mRSVP-TE Interworking Reference Model
mPMBR
  PIM and MPLS interfaces
  Quasi-PIM Interface (QPI)
    Same as PIM Interface But
    No PIM Adjacency
  PIM-MPLS Interworking (PMIW)
    Mapping PIM Forwarding States
PIM States That Terminate at mPMBRs
  Hello
  Assert
PIM States Mapped Between PIM and MPLS
  PIM Forwarding States
    Per-Interface
    Non-Interface Specific
PIM States Uni-casted Using Raw IP
  Register, CRP-Adv
Bootstrap: A Bootstrap Channel Over MPLS
PIM
Site
Multicast Control Information
IP Multicast data
Note:
PIM
PIM
mFIB
PMIW
mPMBR
MPLS
mLIB
PIM
PIM Interface
MPLS Tunnel
QPI
Notes: <number>

## Slide 7
Mapping PIM States To/From MPLS States
PIM
Non-Interface
State
At Leaf PMBR
MPLS In-Band
Data
(M-Flow Specs)
Mapping
PIM
Per-Interface
State
MPLS In-Band
Data
(M-Flow Specs)
Mapping
At Root PMBR
PIM Forwarding States
(*, *, RP)
(*, G)
(S, G)
(S, G, RPT)
MPLS In-Band Data
M-Flow Specs
Binding To P2MP LSP
Policy-based Aggregation
Notes: <number>

## Slide 8
MPLS-PIM Interworking
Leaf mPMBR
  Bind A Prospective PIM Upstream State to A Tunnel
    Initiate Tunnel Signaling If Necessary
      M-Flow Spec as In-Band signaling data
      Create a QPI after success
    May Bind to An Existing Tunnel
      Merge M-Flow Spec
  Create PIM Upstream state
    QPI as RFP Interface
Root mPMBR
  Newly Received M-Flow Specs Mapped to New Per-Interface States
    Create QPI for Each New Tunnel
    QPI as the downstream interface
Transit LSR
  Decide Branching
    Merge M-Flow Specs For Branching LSR
  Pass On In-Band M-Flow Specs Until They Are Not Needed
Notes: <number>

## Slide 9
PIM Bootstrap Over Backbone MPLS
Bootstrap MP2MP Tree
  At Startup, each mPMBR does:
    Designate A Root BSTRAP_ROOT
    Each mPMBR
      Join (BSTRAP_ROOT, ALL_PIM_ROUTERS)
PIM on mPMBR sends and receives Bootstraps
  To/From the channel
  To/From PIM neighbors
BOOTSTRAP
ROOT
BSR1
C-RP(G)
C-RP(G)
Bootstrap
BSR1
…
BSR2
Bootstrap
BSR2
…
Notes: <number>

## Slide 10
Outline
Problem Overview
An Interworking Approach
Q’s & A’s
Notes: <number>