## Slide 1: IGMP and MLD Optimizations in Wireless and Mobile Networks
<number>
draft-liu-multimob-igmp-mld-wireless-mobile-02
Liu Hui Mike McBride
Notes: <number>

## Slide 2: Aims
Optimize IGMP and MLD to meet wireless/mobile multicast network requirements:
  Adaptive to link conditions
  Minimizing group join/leave latency
  Robust to packet loss
  Reducing packet exchange
  Avoiding packet burst
Limit the changes within the protocol framework without introducing interoperability issues
Possibly used in wired network where efficiency and robustness are required
<number>
Notes: <number>

## Slide 3: Option List
<number>
Switching between unicast and multicast Queries
General Query supplemented with unicast Query
Retransmission of General Query
General Query suppression with no receiver
Tuning response delay according to link type/status
Triggering report and query quickly during handover
Notes: <number>

## Slide 4: Switching Between Unicast and Multicast General Queries
<number>
Switch between unicast and multicast General Queries according to actual network conditions
  Unicast query each receiver when number of receivers is small; multicast query all receivers when the number is large
  A switching threshold should be predefined
  Explicit tracking is required to know the reception status
Benefits
  Take advantages of both unicast and multicast Queries
  Unicast Query has less effect on non-members and helps to improve battery-saving
Notes: <number>

## Slide 5: General Query Supplemented with Unicast General Query
<number>
Send unicast Query to each non-respondent valid receivers after a round of General Query, presumably the number of non-respondent receivers is small
Triggered at the end of the [Maximum Response Delay] after General Query, transmitted for [Last Member Query Count] times spaced by [Last Member Query Interval]
Require explicit tracking to track reception status
Benefits:
  Improve robustness without influencing other receivers
Notes: <number>

## Slide 6: Retransmission of General Query
<number>
If after a General Query no response can be collected from all valid receivers, for the reasons e.g.:
  All valid receivers leave the group silently
  All responses of the receivers happen to be lost
  The query fails to reach the other side of link to the receivers.
Retransmit General Queries for [Last Member Query Count] times spaced by [Last Member Query Interval] before deciding to stop General Query totally
Require explicit tracking to acquire the reception status
Benefits
  Improve robustness of General Query if there are valid members
  Realize fast leave if all receivers quit.
Notes: <number>

## Slide 7: General Query Suppression with no Receiver
<number>
Suppress General Query if there is no valid multicast receiver on an interface:
  When the last member reports its leave, by an explicit-tracking router checking its membership database, or by a non-explicit-tracking router getting no response after sending Group-(and-Source-) Specific Queries
  When the (only) member on a PTP link leaves
  When a router after retransmitting General Queries on startup fails to get any response
  When a router previously has valid members but fails to get any response after several rounds of General Queries.
Benefits
  Eliminating unnecessary continuous General Queries has benefit for all terminal on the link for battery saving
Notes: <number>

## Slide 8: Tuning Response Delay according to link type and status
<number>
Tuning Maximum Response Delay according to link type and status, according to the expected number of responders, and link type/status:
  If the expected number of reporters is large and/or the link condition is bad, select larger [Maximum Response Delay]
  If the expected number of reporters is small and/or the link condition is good, select smaller Delay
  If link mode is PTP, choose smaller Delay; or if link mode is PTMP or broadcast, configure larger Delay
Benefits
  By making balance between reducing message burst and leave latency to improve overall protocol performance
Notes: <number>

## Slide 9: Triggering Reports and Queries during handover
<number>
Access router triggers a multicast or unicast General Query as soon as it detects a new terminal on its link
Terminal triggers a Report as soon as it detects its connection to a new network, if it is just in multicast reception state
Benefits
  Enable new access network acquire terminal’s membership and deliver the content quickly, to help reducing disruption or performance deterioration
Notes: <number>

## Slide 10: Changes to ver-01
<number>
Complete the ‘Security Considerations’ section
Delete ‘leaving the network without notification (sec.3.2) ’ and ‘moving out of range (sec. 3.3)’ as the reasons for additional querying
Remove ‘prolonged interval method’ for not introducing big changes to protocol manner
Others be mostly editorial changes, including improving description and updating references
Notes: <number>