## Slide 1: IGMP/MLD-Based Explicit Membership Tracking Function for Multicast Routers draft-ietf-pim-explicit-tracking-01
Hitoshi Asaeda
Nicolai Leymann
84th IETF, July 2012, Vancouver, Canada
<number>
84th IETF, July 2012

## Slide 2: Objectives
The explicit tracking function on routers works for:
  Per-host accounting
  Reducing the number of transmitted Query and Report messages
  Shortening leave latencies
  Maintaining multicast channel characteristics (or statistics)
<number>
84th IETF, July 2012

## Slide 3: Open Issues in Interoperability with Non-supported Routers
In case when querier enables exp. tracking but non-querier does not support it
  Querier does not query to confirm the last member (when it knows there are other members), but non-querier (who is a forwarder but does not know other members) may prune the state?
84th IETF, July 2012
<number>
S
Querier
Forwarder
R1
R2

## Slide 4: Open Issues in Interoperability with Non-supported Routers
Possible solutions
  Disable exp. tracking function when adjacent router(s) exists or “I am not the forwarder”?
    Existence of adjacent router is known when [Other Querier Present Interval] is not 0?
    But routers SHOULD be able to configure disabling this disable function to avoid DoS
  Define new IGMP/MLD message for informing that querier/non-querier(s) enables/disables exp. tracking and synchronizing the behavior?
  Work well for the standard IGMP/MLD without doing anything?
    Other Querier Present Timeout = Rob_Var (2) x Query Int. (125 sec.) x Query Response Int. (10) x 1/2 = 1250 sec.
    Tuning Other Querier Present Timeout shorter (e.g., 10 sec.) ?
84th IETF, July 2012
<number>

## Slide 5: Next Step
Intended status
  Informational RFC ?
Address open issue
  Interoperability
WGLC after revision ?
<number>
84th IETF, July 2012