## Slide 1: draft-lts-pim-hello-mtu-01
PIM MTU Hello Option
for PIM Message Encapsulation
Liu Hui Tina Tsou

## Slide 2: Changes from ver-00
Add comparison of MTU option and PMTU according to comments being collected (Sec.1):
    Running for control plane vs. data plane
    Processing protocol message vs. multicast data
    Exchanging among one-hop PIM neighbors vs. on the whole forwarding paths
    Applied on each PIM router vs. only on head-end
Adding RFC1191 to reference default MTU (Sec.3)
Updating acknowledgment list
Other editorial revisions for illustration

## Slide 3: Problem Statement
PIM message segmentation is common since the number of group states are often large
PIM router only uses its own outbound sending link MTU to calculate message length
If sending (e.g. downstream) MTU is larger compared to receiving (e.g. upstream) MTU, PIM message will be discarded resulting in unsuccessful channel setup, by field report

## Slide 4: Solution
Enable PIM to know MTU information of its neighbor(s) by exchanging Hello messages
Take neighbor link’s MTU into account when segmenting a PIM message
Procedures:
    Define a new MTU option for Hello message
    Introduce ‘Sending MTU State’ recording the minimum value of my outbound MTU and my neighbors’ inbound MTUs on the same link
    Refer to Sending MTU State during the encapsulation

## Slide 5: MTU option
Carried in Hello message by MTU-capable router
Accepted when having a valid value (e.g. not too small) and from a legal neighbor
Ignored by MTU-incapable router

## Slide 6: Scope
All variants of PIM protocols, including PIM-SM,-SSM, -BIDIR, and -DM
Applied to per-hop multicast PIM message
Not applied to unicast Register-like messages, whose MTU issue has already been considered