## Slide 1: PPSP Base Tracker Protocol
draft-cruz-ppsp-base-tracker-protocol
PPSP WG
IETF 84 Vancouver
Yingjie Gu (presenter)
Rui Cruz, Mário Nunes, Jinwei Xia, João Taveira, Deng Lingli

## Slide 2: Protocol Design
The PPSP Base Tracker Protocol is used to control information about which Peers can provide streaming content.
The protocol design supports distributed tracker architectures, providing robustness to the streaming service in case of individual tracker node failure.
The PPSP Base Tracker Protocol is a request-response protocol.
  Requests are sent, and responses returned to these requests.
  A single request generates a single response.
The Tracker Protocol design does not require Peers to be “connected” to the tracker all the time
The Tracker can provide NAT traversal services (STUN-like Tracker) by discovering the public transport address candidate of a Peer via PPSP Tracker Protocol messages

## Slide 3: Protocol Overview
The Base Tracker Protocol uses two messages for the operation:
  a CONNECT Request message to “register” and/or request actions on swarm(s) of streaming contents;
  a STAT-REPORT Request message to periodically inform the Tracker about its status and supply statistic information;
To terminate all its activity in the P2P streaming service the Peer may:
  Send a CONNECT Requesting action to LEAVE swarm(s);
  Stop sending periodic STAT_REPORT;

## Slide 4: A typical PPSP Session
A peer CONNECT to the system and request action to join swarm x.

## Slide 5: A typical PPSP Session
A peer Seeder CONNECT or re-CONNECT to the system and simultaneously joins swarms x, y, z.

## Slide 6: Request Messages
CONNECT:
  used when a Peer first “registers” to the system and request “actions” on swarms;
  if already registered, to request further “actions” on swarms;
    The Peer provides its Peer-ID, and the IP addresses on its interfaces (IPv4, IPv6).
    The Peer provides “actions” on one or more swarm(s)
    The Tracker records the Peer-ID, connect-time, peer IP addresses and link status.
    The tracker checks if Peer is LEECH or SEED in swarm “actions” requested and updates the Peer-ID to the peer lists.
  The method allows a security layer to be established between the Peer and the Tracker.

## Slide 7: CONNECT Request example
Switch swarms (JOIN 2222, LEAVE 1111):
LEAVE
JOIN

## Slide 8: CONNECT Response example
Peer List for swarm 2222:

## Slide 9: Request Messages
STAT_REPORT:
  used by a Peer to inform the Tracker on statistic and status data:
    Is initiated by the peer, periodically while active.
    May contain activity statistics.
  When not including statistics data, behaves as a keep-alive signal to the tracker.

## Slide 10: STAT_REPORT example

## Slide 11: Per-Peer-ID STATE MACHINE

## Slide 12: Extensions and Implementation
The protocol is designed such that it can be extended for enhanced functionalities
Guidelines for extending are provided in the draft
An Extended, retro-compatible version was already submitted as:
  draft-huang-ppsp-extended-tracker-protocol
Protocol implemented in C language

## Slide 13
The Authors would like to ask for the Base Tracker Protocol defined in this draft to be adopted as PPSP Working Group item

## Slide 14: Thank You !
Comments are welcomed!