## Slide 1: IETF 84 – Vancouver, Canada Transparent SDH/SONET over Packet (draft-manhoudt-pwe3-tsop-00)
G. Manhoudt -- gmanhoudt@aimvalley.nl
S. Roullot -- stephan.roullot@alcatel-lucent.com
P. Roberts -- peter.roberts@alcatel-lucent.com

## Slide 2: Problem Statement
A Pseudowire mechanism for STM-N/OC-M transport is needed, which
  Allows integration in small NID or SFP,
  Has minimal network management impact, and,
  Is transparent for STM-N (incl. Section OH & Sync)
Today’s solution RFC 4842 (CEP):
  Requires full STM-N termination in PE
  Maps VCs in different PWs (to different destinations)
  Breaks STM-N management path (D-bytes), APS channel (K-bytes) and Section PM (B2, M1 bytes)
  Normally not transparent to SDH synchronization

## Slide 3: Proposed solution: TSoP
TSoP carries STM-N transparently over MPLS
  Architecturally comparable to STM-N over OTN transport
1-to-1 relation between STM-N client and TSoP PW
TSoP is modeled after SAToP (RFC 4553)
  Same Control Word and RTP Header specification
Characteristics:
  No STM-N overhead termination
  Segments STM-N bitstream in equal sized packets
    810 bytes
  Only client signal bitrate is relevant
TSoP supports SDH (STM-N) and SONET (OC-M)

## Slide 4: TSoP nomenclature
PSN
PE2
PE1
CE1
(SDH)
CE2
(SDH)
AC1
(STM-N)
AC2
(STM-N)
TSoP PW
over MPLS
TSoP Pseudowire
CE-bound IWF
( TSoP receiver)
PSN-bound IWF
(TSoP sender)
STM-N/OC-M (multiplex) section

## Slide 5: Discussion: Timing transparency?
TSoP sender MUST insert RTP header
TSoP receiver MUST:
  Maintain STM-N bit-count (using SQN)
  Meet G.825/GR-253 jitter and wander requirements
  Generate 20 ppm G-AIS during failures
TSoP receiver implementation is not prescribed
  Adaptive, differential or other schemes allowed
  “Quality” of TSoP receiver clock not further specified
  Appendix with design considerations can be added

## Slide 6: Proposed next steps
Remove IP/UDP transport option from draft?
Address comments from pwe3 list discussion
  Add an appendix on timing transparency in relation to RFC 4197 synchronization scenarios
Liaise to ITU-T SG15
  Next meeting: September 10-21, 2012, Geneva
Request adoption as WG draft after inclusion of ITU-T feedback