## Slide 1: Virtual Circuit Connectivity Verification version 2 (VCCV2) draft-nadeau-pwe3-vccv2-00.txt
Thomas Nadeau
Yaakov Stein
Carlos Pignataro
IETF 84 - Vancouver
<number>
Notes: <number>

## Slide 2: Motivation
Virtual Circuit Connectivity Verification (VCCV), the pseudowire OAM mechanism is described in RFC5085, RFC5885, and ietf-pwe3-vccv-for-gal.
This mechanism has been widely implemented and deployed, but it has been reported [I-D.ietf-pwe3-vccv-impl-survey-results] that the large number of VCCV options has led to interoperability issues.
<number>

## Slide 3: Present CC State of Affairs
RFC5085 together with ietf-pwe3-vccv-for-gal define four Control Channel (CC) types for MPLS PWs:
Type 1 using the control word (CW),
Type 2 using the Router Alert label (label=1) above the PW label,
Type 3 using TTL expiry,
Type 4 using G-ACh Label (label=13 [RFC5586] below the PW label.
<number>

## Slide 4: Placement of the RA and GAL
We should understand that we are obsoleting the "label above the PW label” in favor of the "label below the PW label".
<number>

## Slide 5: Goals for CC Types
Reduce down to 2 CC types
we are giving (or going to give) guidelines for when to use which.
<number>

## Slide 6: Final Document Structure
Is this draft is supposed to be short and sweet of a rewrite of VCCV with all the details in one place?
A short document that obsoletes RA only?
A –bis version that consolidates all of the existing RFCs/drafts including MPLS-TP? This would normatively redefine all CC Types
  type 2 as obsolete, type 1 as mandatory for CW, type 4 as mandatory for non-CW, and a variation of type 3 (manipulating TTL) as for multi-segment only
-<number>