## Slide 1: PW Endpoint Fast Failure Protection draft-shen-pwe3-endpoint-fast-protection-02
Yimin Shen (Juniper Networks)
Rahul Aggarwal (Arktan Inc)
Wim Henderickx (Alcatel-Lucent)
IETF 84, Vancouver, BC, Canada

## Slide 2: Motivation
It is desirable to have local repair mechanisms protect every link/node along a data path.
  Fast failure detection.
  Fast traffic restoration – 10s of milliseconds.
  Can complement global repair.
This draft addresses the need for such a mechanism for egress AC, egress PE, and switching PE.
CE1
CE2
PE1
PE2
PW
S-PE1
seg-1
seg-2
traffic
AC
AC

## Slide 3: Mechanism
Fast protection mechanism based on local repair.
  Single-segment and multi-segment PWs.
  RSVP-TE, LDP and IP tunnels as transport and bypass tunnels.
Based on upstream label assignment, context-specific label switching, redundant PWs, and multi-homed CEs.
  PW label replication from primary PE to protector, via an LDP extension.

## Slide 4: Mechanism (cont.)
Primary PE distributes PW labels to protector.
Protector installs primary PE’s PW labels in a context-specific label table.
PLR detects failure, and redirects traffic via a bypass tunnel, with PW label intact.
Protector forwards PW packets based on the context-specific label table.
Co-located protector model and centralized protector model.
Context ID
  Identifies the pair of <primary PE, protector>.
  Indicates the primary PE’s label space to the protector.
  Serves as destination of transport tunnel and bypass tunnel, and facilitates path computation.

## Slide 5: Updates
Generic PSN layer - RSVP-TE, LDP, and IP.
Relationship between local repair, global repair, and C-plane convergence.
  Local repair and global repair complement each other.
  A bypass tunnel is not affected by the topology changes resulting from the failure. It can be used to repair traffic, before global repair and C-plane convergence.
  Global repair and C-plane convergence have the responsibility to move traffic to a fully functional PW over a fully functional transport tunnel.

## Slide 6: Example 1: Egress AC failure
PLR is the primary PE (PE2). It establishes a bypass to protector (PE4).
Protector (PE4)
  Learns primary PW’s label X (upstream assigned label) from PE2 via LDP.
  Installs a FIB entry for label X in a context-specific label space. Nexthop is CE2.
  Assigns a UHP label Y for the bypass, pointing to this label space.
Local repair:
  PE2 redirects PW packets through the bypass.
  PE4 receives packets with outer label Y and inner label X.
  PE4 looks up label X in the context-specific label space, and sends packets to CE2.
CE1
CE2
PE1
PE2
PLR
PW1 (primary, label=X)
PW2 (backup)
PE4
protector
PE3
Bypass
label=Y

## Slide 7: Example 2: Egress PE failure
PLR is the penultimate hop router. It establishes a bypass to protector (PE4).
Protector (PE4)
  Learns primary PW’s label X (upstream assigned label) from PE2 via LDP.
  Installs a FIB entry for label X in a context-specific label space. Nexthop is CE2.
  Assigns a UHP label Y for the bypass, pointing to this label space.
Local repair:
  PLR redirects PW packets through the bypass.
  PE4 receives packets with outer label Y and inner label X.
  PE4 looks up label X in the context-specific label space, and sends packets to CE2.
CE1
CE2
PE1
PE2
PE3
PE4
protector
PW1 (primary, label=X)
PW2 (backup)
PLR
bypass
label=Y

## Slide 8: Example 3: Switching-PE failure
PLR is the penultimate hop router of seg-1. It establishes a bypass to protector (S-PE2).
Protector (S-PE2)
  Learns primary PW’s label X (upstream assigned label) from S-PE1 via LDP.
  Installs a FIB entry for label X in a context-specific label space. Nexthop is seg-4.
  Assigns a UHP label Y for the bypass, pointing to this label space.
Local repair:
  PLR redirects PW packets through the bypass.
  S-PE2 receives packets with outer label Y and inner label X.
  S-PE2 looks up label X in the context-specific label space, swaps label to Z, pushes the label of a transport tunnel to PE4.
CE1
CE2
PE1
PE2
PE3
PE4
PLR
bypass
label=Y
S-PE1
S-PE2
protector
seg-3
seg-4, label=Z
seg-2
seg-1, label=X

## Slide 9: Next Steps
Questions and comments?
WG adoption?