## Slide 1: Static pseudowire configuration checking using Generic Associated Channel (G-ACh) Advertisement Protocol
Authors:
Lizhong Jin
Ran Chen
Sami Boutros
Sriganesh Kini
<number>
draft-jc-pwe3-static-config-check-00
Presenter:
Sami Boutros
IETF84, July 2012
Notes: <number>

## Slide 2: What updates?
draft-jc-pwe3-mpls-tp-static-checking-00 was presented at IETF83 Paris meeting, and received comments from meeting and mailing list.
draft-jc-pwe3-static-config-check-00 is the updated version of draft-jc-pwe3-mpls-tp-static-checking-00.
Updates include:
  Extend static PW checking for both MPLS-TP and Non-TP;
  New Static PW FEC Element TLV is defined, instead of using Generalized ID FEC;
  TX/RX Sequence number is used to ensure message delivery, instead of using local and remote PW element.
  Control word configuration checking update;
<number>

## Slide 3: Extensions to GAP
GAP is defined in draft-ietf-mpls-gach-adv-02.
The extensions to GAP include:
  New GAP application "static PW" is defined.
  Application Data Block (ADB) for "static PW" application is defined with “Static PW FEC Element TLV”.
  Define static PW suppress TLV to suppress static PW FEC element transmission.
<number>

## Slide 4
<number>
Format of Static PW FEC Element TLV

## Slide 5: Sending PW application Element TLV
When a PW is configured, the PE MUST send its local PW configuration information using the GAP over the PSN tunnel.
  Set the TX sequence number to a non-zero value;
  RX sequence number MUST be set to the previously received TX sequence number, otherwise set to zero;
<number>

## Slide 6: Receiving PW application Element TLV
If PE has local PW configuration and previously sent GAP, it MUST check RX seq# received and TX seq# it previously sent.
  If equal, send GAP message with static PW suppress TLV
  Otherwise, do not send GAP message with static PW suppress TLV
If there is no local PW configuration, the receiving PE MUST retain the remote static PW FEC Element information.
<number>

## Slide 7: Message process
<number>
PE-A
PE-B
GAP Message with TX seq_A
GAP Message with TX seq_B
and with RX seq_A
Suppress message for PW
Suppress message for PW
Config local PW info A
Config local PW info B
Check TX&RX seq#:
A has received B;
B has received A,
tell peer to not send
Check TX&RX seq#:
B has received A;
A has received B,
tell peer to not send
GAP Message with TX seq_A
and with RX seq_B
Receive remote PW info A
Stop sending GAP
Stop sending GAP
Continue sending GAP

## Slide 8: Other Procedure
Configuration check process:
  Check control word, MUST do logical operation "AND".
  Check PW type and negotiate interface parameters as specified in [RFC4447].
  Check incoming and outgoing static PW labels.
Remote Label Advertisement
  The received incoming label from GAP could be used by the remote PE as the outgoing label for the PW.
<number>

## Slide 9: Next steps
Any more comments are appreciated.
Ready for WG adoption.
Thank you
<number>