## Slide 1: IETF 84 – Vancouver August 2012
LSP Ping Support for P2MP PWs
(draft-jain-pwe3-p2mp-pw-lsp-ping-00.txt)
Parag Jain (Cisco Systems Inc.),
Sami Boutros (Cisco Systems Inc.),
Sam Aldrin (Huawei Technologies)

## Slide 2: LSP Ping Support for P2MP PW
Define LSP Ping procedures for P2MP PW
P2MP PWs can be signaled using LDP or BGP
Supports Inclusive and Selective P2MP MPLS P-trees
Supports MLDP and P2MP TE P2MP MPLS P-trees
Define a new FEC 130 Pseudowire sub-TLV for Target FEC Stack to identify P2MP PW under test
Support for Echo Reply using the downstream assigned P2P MPLS label signaled in the Label Mapping message of the P2MP PW message

## Slide 3: Proposed FEC 130 Pseudowire Sub TLV Format
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0| PW Type | AGI Type | AGI Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
̃ AGI Value ̃
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| AII Type | SAII Length | SAII Value |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
̃ SAII Value (continued) ̃
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
IANA is requested to assign a sub-TLV type value of 24 from the "Multiprotocol Label Switching (MPLS) Label Switched Paths (LSPs) Parameters - TLVs" registry, "TLVs and sub- TLVs" sub-registry.

## Slide 4: Operations
For Inclusive P2MP MPLS P-trees, the echo request is sent using the P2MP MPLS P-tree label.
For Aggregate Inclusive P-trees, the echo request is sent using a label stack of <P2MP MPLS P-tree label, upstream assigned P2MP PW label>. The P2MP MPLS P-tree label is the top label and upstream assigned P2MP PW label is bottom label.
P routers swap the P2MP MPLS P-tree label
Bud/Tail PEs, performs the checks for the FEC 130 Pseudowire sub-TLV present in the Target FEC Stack TLV as described in Section 4.4 in [RFC4379] and respond according to [RFC4379] processing rules

## Slide 5: Echo Reply using Downstream Assigned Label
Root of a P2MP PW may send an optional downstream assigned P2P MPLS label in the LDP Label Mapping message for the P2MP PW signaling.
If the root of a P2MP PW expects leaf to send echo reply using the downstream assigned label signaled in the Label Mapping message of the P2MP PW message, LSP Ping Reply Mode [RFC4379] in the LSP Ping echo request should be set to 4 “Reply via application level control channel”.

## Slide 6: Controlling Echo Responses
Use Echo Jitter TLV defined in draft-ietf-mpls-p2mp-lsp-ping-17 for preventing congestion of Echo Responses.
Use Node Address P2MP Responder Identfier TLV defined in draft-ietf-mpls-p2mp-lsp-ping-17 for limiting the Echo Reply to a single egress node.

## Slide 7: Next Steps
Seeking Feedback
Looking for WG adoption
.