## Slide 1: MPLS-TP Pseudowire Configuration using OpenFlow 1.3
draft-medved-pwe3-of-config-02
J.Medved
A.McLachlan
D.Meyer

## Slide 2: Draft Summary
This draft is aimed 2 main area:
  Provisioning of Pseudowires in the MPLS-TP environment. (We are not covering the Transport LSP at this point)
  OAM setup over the data path for the Pseudowires we are configuring.

## Slide 3: Method Summary
A PW is to be configured between an ingress and an egress attachment circuit.
Using an external OpenFlow Controller we provision the PW between the 2 end points.
Using OpenFlow rules we direct the desired packets into this PW.
Also using Open Flow rules we direct the OAM packets into the OAM Engine, or return them if they require, echo-mode bfd for example.
Redundancy uses the OpenFlow Group port as a fast-fail mechanism.

## Slide 4: Thoughts behind it
Why have we considered OpenFlow for this?
  We wanted to enhance the programmatic operations of an MPLS-TP element.
  OpenFlow can work well in this environment, due to its ability to program switching elements.
  As it is an Open Standard it seems to fit well as part of an SDN approach for configuring PWs in the MPLS-TP environments.

## Slide 5: What issues does this draft address?
Some carriers have expressed a desire to have an open non-vendor specific provisioning. Neither CLI driven nor a vendor related provisioning platform.
OAM was a key requirement:
  As OpenFlow 1.3 does not include OAM, we wanted to show how we can use OF rules to direct OAM packets to an independent OAM engine.