## Slide 1: Multicast Forwarding in LLNs (draft-ietf-roll-trickle-mcast-01)
Jonathan Hui
Richard Kelsey
ROLL WG Meeting
84th IETF Meeting
Vancouver, Canada

## Slide 2: History
2011-04-11: draft-ietf-roll-trickle-mcast-00
  Expired 2011-10-13
2012-07-13: draft-ietf-roll-trickle-mcast-01
  No changes to content

## Slide 3: Overview
Problem
  Forward IPv6 multicast messages without maintaining a multicast forwarding topology
Solution
  Flood (disseminate) IPv6 multicast messages
  All devices in LLN receive the message

## Slide 4: Dissemination Overview
On receiving a message
  If “new” message,
    retransmit the message,
    pass to upper layers if subscribed to mcast group
  Otherwise, drop message
What is “new”?
  IPv6 HbH Option (SeedID, SeqNo)
  SeedID: device that initiates dissemination
  SeqNo: duplicate detection, message ordering

## Slide 5: Retransmission Strategies
Simple flooding (low latency)
  Retransmit N times
Controlled dissemination (low redundancy)
  Trickle [RFC6206]
    Adaptive transmission timing
    Redundant transmission suppression
  Advertise summaries rather than actual data messages
Trickle parameterization
  Simple flood: set k to infinity (no suppression)
  Controlled dissemination: set k to small value

## Slide 6: Sliding Windows
Disseminate multiple messages from same SeedID
  Receiving messages out of order will filter old messages
Sliding window
  Bounded history to allow some out-of-order
  May size window based on memory constraints

## Slide 7: Implementations
ZigBee
  Component of SEP 2.0
  Implementation by several vendors
  Simple flooding used with mDNS
Cisco
  Simple flooding and controlled dissemination
Peter van der Stok
  Controlled dissemination in simulation
Others?

## Slide 8: Next Steps
IPv6-in-IPv6 Encapsulation
  Insert/remove HbH Option
Reserve bits for straightforward evolution
  Flags/version/etc.
Incorporate suggestions in draft-vanderstock-roll-mcreq
Add more text, tighten up specification, etc.
More feedback from WG!