## Slide 1: DSCP markings for RTCWeb QoS draft-jennings-rtcweb-qos-00
IETF 84
Subha Dhesikan, Dan Druta, Cullen Jennings, Paul Jones, James Polk

## Slide 2: What we are talking about …
RTCWeb browsers are sending audio / video in RTP
The RTP packet has some bits that get set with DSCP
Some times we might have explicit information on how to set this, but in other cases, the browsers need a default value to use
Just doing what existing RFC say …
  Consistent with RFC 4594, draft-polk-tsvwg-rfc4594-update, other SDO etc
  Not trying to change anything other than give clear guidance

## Slide 3: Where this helps …
Does not help everywhere or all the time
Does not break things
Seen to help for congestion on broadband (DLS, Cable ) uplink
Seen to help for congestion on local WIFI wireless
Been told it helps on LTE ( see draft-ejzak-avtcore-rtp-subsessions - 3pm today AVTCORE )
Some enterprise networks
Unlikely to help on broadband (DSL, Cable) downlink but possible that could change over time if endpoints did this

## Slide 4: Setting the DSCP
Browser (not the Java Script) sets the media type
Java Script provides the relative importance
These are used to pick default DSCP
| | Low | Medium | High |
+-----------------------+-----------+-----------+-----------+
| Interactive Audio | 46 (EF) | 46 (EF) | 46 (EF) |
| Interactive Video | 38 (AF43) | 36 (AF42) | 34 (AF41) |
| Data | 8 (CS1) | 0 (BE) | 10 (AF11) |

## Slide 5: Why three levels?
Not enough DSCP per hop behaviors defined for more than 3
Need at least two for existing use cases
Some people want three so can do cool measurement based QoS things. Some people want three for other reasons. Some people think is more is better than less.
Some people think 2 is enough.
Have not heard any argument that 2 would be better than 3.

## Slide 6: What this draft is suggesting
The browser should set the DSCP as described in RFC 4594 (4594update is same for these parts)
The input to set the DSCP in the browser is split between the Java Script application and browser media engine. Each contributes to the part they know
Implication to W3C API would be that there needed to be a way to for API to indicate relative priorities of media
Also want a way for JS to find out markings being used when media is sent

## Slide 7: Next Steps
When I am chairing WGs, I really hate that every presentation seems to end with
  CAN WE ADOPT THIS AS WG ITEM
As an individual contributor, I really hate when we get 100 people in a room, spend 20 minutes discussing something, then make no decisions and say
  Take It To The List
where absolutely nothing will happen until the next meeting