## Slide 1: Codec Control
draft-westerlund-rtcweb-codec-control
Magnus Westerlund
Bo Burman

## Slide 2: Outline
Problem Statement
Model
  SDP/JSEP
  COP
  Browser Focused
Parameters
Benefits
Choices

## Slide 3: Problem Statement
The encoding of a media source is sent from A to B in a PeerConnection (PC)
B uses the media as the application in B determines
How to ensure that what A delivers is as useful to B as possible?
  Video at suitable resolution
  Video at suitable frame-rate
  Audio at appropriate audio bandwidth,
  Audio with the appropriate number of channels
  Using the most suitable codec
Transport limitations must be taken into account
  Affect trade-off between multiple media streams
A
B
PC

## Slide 4: Problem STATEMENT
Centralized Conferencing
  A sends media to Mixer, mixer forwards to B-E
  Mixer will try to optimize media across the receivers
  Codec control enables best possible single rate
  Codec control and Simulcast must be possible to combine to optimize multiple operations points
Multiple Media Streams
  Receiver may receive multiple media streams (tracks)
  Application may use the tracks differently and at different fidelities
  Must enable stream specific control
A
B
Mixer
C
D
E

## Slide 5: Solution Model
Use SDP/JSEP to negotiate outer boundaries for media
  Using RTP Payload parameters to establish receiver capabilities
    Video Codec profile and levels
    Audio sampling rate, codec modes, etc.
  SDP Bandwidth Parameters
    b=AS establish maximum bit-rates for media streams
  Use Image Attribute (RFC6236) to indicate the set of preferred video resolutions
    Per SSRC values are not required
  Changes rarely
Use Codec Operations Point (COP) for dynamic changes during the session
  draft-westerlund-avtext-codec-operation-point-00
  IPR Statement: https://datatracker.ietf.org/ipr/1793/

## Slide 6: Solution Model
COP: Notification
Use Codec Operation Point (COP) RTCP mechanism
  Media Receiver request preferred codec parameters
    Parameters MUST be within envelop defined by SDP
  Media Sender matches request as good as possible based on limitations
    Available bit-rate
    Encoder limitations
    Multi-party considerations, i.e. media stream used by many
  Request per media stream
  Frequent request for parameter changes are possible
  COP is an extensible framework allowing for new parameters
A
B
RTP
COP: Request
COP: Notification
RTP

## Slide 7: Solution Model
Media receiving browser determines when to request changes
  Based on application’s actual usage of media
  Any API knobs, Constraints or Methods
Media Sending browser may change at any time based on the aggregate of all input
  COP
  Session parameters
  Congestion Control
  JS Application
Enables media stream optimizations for all applications, not only the advanced ones
  Advanced applications influence depends on the API knobs

## Slide 8: Benefits
Always using Peer to Peer Path, thus minimal Delay
COP requests only in media plane, goes to central node or source
Minimal Overhead
  COP messages are small and can be sent as stand alone RTCP packets
  No extra processing by comparing entire SDP to determine if there are other session changes as JSEP would require
No blocking due to outstanding requests
  JSEP/SDP can’t send updated parameter or session changes when an Offer is outstanding
Available for all applications
  Will work in also simple applications thanks to browser side implementation
  Advanced control will depend on what API functions are provided in W3C
Supports handling of multiple operation points
  Supports Simulcast or Scalable Codecs
Easily Extendable for additional Parameters in the future

## Slide 9: Parameters
We propose the following parameters for WebRTC:
  Codec
    Payload Type
    Framerate
    Horizontal Pixels
    Vertical Pixels
    Bitrate
    Token Bucket Size
  Transport
    Maximum RTP Packet Size
    Maximum RTP Packet Rate
    Application Data Unit Aggregation

## Slide 10: Choices
Main choice in Codec Control
  Signaling only
  Signaling and COP based solution
If COP is included
  Then the parameters to support must be chosen
    Additional could be proposed to be specified
  Ensure that specification is produced in timely fashion
Is SSRC specific usage of a=imageattr needed?
  Not needed if COP is chosen