## Slide 1: Interface to The Internet Routing System (IRS) draft-atlas-irs-problem-statement-00 draft-ward-irs-framework-00
Alia Atlas
Thomas Nadeau
David Ward
IETF 84 – Routing Area Open Meeting

## Slide 2: What’s the Problem?
Applications Need To Dynamically
  And Knowledgeably, based on:
    Topology (active & potential)
    Events
    Traffic Measurements
    Etc.
  Augment Routing, based on:
    Policy
    Flow & Application Awareness
    Time & External Changes
Network
Application
Feedback Loop:
Control & Information

## Slide 3: What’s Needed for the Routing System?
Data Models for Routing & Signaling State
  RIB Layer: unicast RIBs, mcast RIBs, LFIB, etc.
  Protocols: ISIS, OSPF, BGP, RSVP-TE, LDP, PIM, mLDP, etc.
  Related: Policy-Based Routing, QoS, OAM, etc.
Framework of Integrating of External Data into Routing
  Indirection, Policy, Loop-Detection
Filtered Events for Triggers, Verification & Learning Changed Router State
Data Models for State
  Topology model, interface, Measurements, etc.
Device-Level and Network-Level Interface & Protocol(s)

## Slide 4: Main Concerns
Standard data-models
  clear self-describing semantics
  Sufficient coverage for use-cases needing feedback
Applications aren’t routers – so can’t need to implement a list of routing/signaling protocols
Good security, authorization, & identity mechanisms
Scaling and responsiveness:
  Multiple applications
  Many operations per second
  Significant data to export, even when filtered

## Slide 5: IRS Framework
Application
IRS Client
Policy Database
Subscription to Events and Configuration Templates for Measurement, Events, QoS, OAM, etc…
IRS Agent
Routing and Signaling Protocols
Topology
Database
RIB Manager
FIB Manager and Data Plane
IRS Protocol
Router
Application
Application
IRS Client

## Slide 6: IRS Interface Key Aspects
Multiple Simultaneous Asynchronous Operations
Duplex Communication
  Asynchronous, Filtered Events
  Topologic Information (IGP, BGP, VPN, active/potential)
High-Throughput
Highly Responsive
Multi-Channel (readers/writers)
Capabilities Negotiation/Advertisement (self-describing)

## Slide 7: What IRS is not
IRS is NOT:
the only configuration mechanism a router will ever need,
a direct replacement for existing routing/signaling protocols,
the only way to read topology androuter data that will ever be needed,
solely limited to a single network device.

## Slide 8: IRS: Focused Scope
Start with a defined scope:
  Small set of data-models (RIB layer) for control
  Set of events to support related use-cases
  Data-model for topology
  Investigate protocol options for the interface
    Consider application-friendly paradigms
    Consider extensions as well as new definitions
  Define set of motivating use-cases to drive this scope.

## Slide 9: Next Steps
IETF 84 - Routing Area Open Meeting
Related drafts:
  draft-atlas-irs-problem-statement-00
  draft-ward-irs-framework-00
Please send detailed feedback to irs-discuss@ietf.org
Questions?