## Slide 1: Power-aware Routing and Traffic Engineering: Requirements, Approaches, and Issues
draft-zhang-greennet-00.txt
Beichuan Zhang, Junxiao Shi, Jie Dong, Mingui Zhang

## Slide 2: The Problem
Increasing energy consumption of network infrastructures
  More network devices: routers, switches, …
  Devices are more power-hungry.
Impacts
  Power delivery
  Cooling
  Financial and environmental
In ISPs, IXPs, data centers, enterprises, …

## Slide 3: The Opportunity
Networks have lots of redundancy
  Redundant links and nodes
  Overprovisioned link capacity
  Load-balancing traffic engineering
Average link utilization is low but all devices are running at full capacity all the time.
  High resiliency, low energy efficiency.
Need a better tradeoff between the two.

## Slide 4: The Solution
Power-aware routing and traffic engineering:
  Depending on traffic level, adjust power states of network devices to reduce energy consumption while delivering packets within certain performance constraints.
This document provides an overview on the solution requirements, approaches, and potential issues.

## Slide 5: Requirements
The network should retain enough resiliency against node and/or link failures.
The network should have enough standby capacity or be able to react quickly enough to traffic spikes in order to minimize packet losses due to links/routers being in low power states.
QoS metrics such as delay, jitter, etc. should be kept at a desired level.
The operation of other protocols should not be interrupted, or at least other protocols should be able to adapt without being broken after links/routers change their power states.

## Slide 6: Sleeping vs. Rate Adaptation
Link sleeping saves more energy but cuts off the connectivity
  Need changes to the control plane.
Rate adaptation save less energy but the connectivity is preserved.
  Control packets can still get through.
They’re not exclusive.
  E.g., Composite links.

## Slide 7: Configured vs. Adaptive
Configure the schedule of router’s power state changes
  Based on long-term traffic average, if it’s relatively stable.
  Easy to do, but not saving as much energy as the adaptive approach.
Adjust power state to dynamically adapt to significant traffic changes.
  Save more energy, more adaptive, but more complicated.
They’re not exclusive either.

## Slide 8: Distributed vs. Centralized
Routers decide their power states in a distributed fashion.
  Fits the traditional Internet operation model
  MUST ensure consistent network states
A central controller decides the power states for all routers
  Fits the new SDN operation model
  Controller can make better decisions with more complete information.
  MUST be protected from controller failure.

## Slide 9: Hardware Support
Hardware should support the control of its power state.
  Sleep/wakeup, rate up/down, etc.
  Reasonable short transition time
  Durable under many transitions.
  Granularity of control
Hardware should support energy-related monitoring and information collection
  Learn the power states, energy footprint, performance, etc.
  EMAN WG.

## Slide 10: Sleeping Links
When a link is in sleep and doesn’t transmit/receive control packets, it will cause problems to other protocols, for examples:
  OSPF regards a sleeping link as a down link due to the missing of HELLOs.
  Multicast protocol too.
Modify protocols to add the support of “sleeping” links?

## Slide 11: Network Resiliency
Higher energy efficiency means less links/bandwidth standing by.
Need to guarantee certain level of resiliency. E.g.,
  A redundancy level of 2 to accommodate single link failures.
  Make sure of existing FRR mechanisms
  Faster link wakeup and/or rate increase when needed.
Minimize packet loss or congestion
  Leave a safe margin in link when making routing/TE decisions.

## Slide 12: Future Work
Research: better routing/TE algorithms
Standardization: add support for power-aware features in network protocols.

## Slide 13: Thanks!