## Slide 1: Some early SIPREC interop testing results
Hadriel Kaplan

## Slide 2: We’ve done some testing
3 Vendors, 4 implementations
  2 SRCs, 2 SRS’
Hopefully going to next Sipit as well
3 Problems found, arguably bugs
Details next...

## Slide 3: Problem 1
SRS implemented older draft XML, but there’s no way to know that by by MIME type
The problem now is how do we know when the SRS gets updated to the correct/latest XML in the future?
  Requires configuration change on SRC and/or SRS
This is a general problem with implementing drafts of course, but the IETF wants early implementation experience/knowledge

## Slide 4: Problem 2
SRC and SRS setup Recording Session successfully, but then both SRC and SRS sent re-INVITEs at the same time (i.e., glare)
  This is supposed to cause a 491/500 response and fail the transaction but not the dialog, and start random timers on both sides
  Naturally that didn’t happen... well it kinda did, but things weren’t good
Might want to put some text in the docs to watch out for this being possible

## Slide 5: Problem 3
SRC and SRS setup Recording Session successfully, but...
Far-end PBX then changes the participant with a SIP UPDATE method, which SRC forwarded correctly to SIP UA, but SRC did not update SRS
  Interestingly, the UPDATE changed the From/PAI URIs of the dialog (yes, that’s legal)

## Slide 6: Other notes
1 SRC created the Recording Session on receipt of INVITE, the other on receipt of SDP answer in 18x/200
  This was a surprise to one of the SRS’
1 SRC actually honored the recordpref attribute
  This was a surprise to me 
  Of course it could be overridden with configuration (not a surprise)

## Slide 7
Has anyone else done interop testing yet?