## Slide 1: Public 4over6: WGLC feedback
Peng Wu
IETF84

## Slide 2: Feedback from WGLC
Relationship with stateless 4-over-6 solutions?
Different primary targets and application scenarios. Public 4over6:
  Keep IPv4-IPv6 addressing independency, for
  Deployment and operation flexibility
    Middle IPv6 infrastructure transparent of the 4-over-6 usage
    Service can be provided in on-demand style
    IPv4 address resources managed in a centralized way
  At the cost of maintaining per-subscriber states
Notes: EA bits=0 not stateless rules not used
Dhcpv6 in map, dhcpv4 centrialized
Map use dhcpv4

## Slide 3: Feedback from WGLC
Relationship with address sharing solution?
Clean solution for full IPv4 address provisioning
  No further implementation to support port-set
    DHCP server: extension for port-set management
    not needed
    Initiator: NAT not necessarily required (app server, enterprise)
    Concentrator: encapsulation based only on IP dst addr
  many ISPs are capable of providing per-subscriber IPv4 addresses
Notes: Shared address cannot be interface addr. ARP
static configuration for address prefix in enterprise case

## Slide 4: Feedback from WGLC
Provisioning steps?
Explicitly describes the provision steps
  Provision IPv6
  Provision concentrator’s IPv6 address (DHCPv6 option RFC6334)
  Provision IPv4 by DHCPv4-over-IPv6

## Slide 5: Updates in -ietf-02
[section 1] Add a paragraph to discuss the relationship with port-set-enabled solutions
[section 1] Add a paragraph in to discuss the relationship with stateless IPv4-over-IPv6 solutions
[section 5.2] Add a paragraph to describe the provisioning steps
[section 5.3] State hairpin support of the concentrator
[section 5.3]Add the IPv4-IPv6 source address binding verification requirement on the concentrator
Change the terminology of "mapping" to "binding", to avoid the possible confusion with "algorithmic mapping"

## Slide 6: Implementation
Tunnel Concentrator Device
  Linux implementation
CPE Initiator Device
  Linux implementation
Host Initiator Client Software
  Linux
  Windows 7
  Windows XP
  Android 4.0 (Under developing)

## Slide 7: Deployment
Concentrator on CERNET2
Different kinds of initiators on Tsinghua Campus
IPv6 Campus
Network
IPv4 LAN
IPv4 Internet
CERNET2
Concentrator
CPE Initiator
Host Initiator
Win7/XP Client
Android
Initiator
IPv6 AP
IPv4 AP

## Slide 8
The new version reflects the feedbacks from WGLC
Next step?