## Slide 1: Lightweight 4over6: An Extension to DS-Lite Architecture draft-cui-softwire-b4-translated-ds-lite IETF 84-Vancouver, August 2012
Y. Cui, Q. Sun, M. Boucadair, T. Tsou, Y. Lee, I. Farrer, et al.

## Slide 2: Technical Matrix of 4-over-6 solutions
Address
Binding
Algorithmic
Mapping
Addr Resource Managed in CGN
Addr/Port Set
Provisioning
Lightweight 4over6
Per-subscriber
stateful
Per-session
stateful
Stateless
Notes: 特点加括号注明，终端感知性
<number>

## Slide 3: Requirements
A solution optimized for the hub-and-spoke use case
  A ‘screwdriver’ not a ‘Swiss army knife’!
Operational simple & clean
Flexible IPv6/IPv4 addressing
Address sharing
Good scalability
Reduced Logging
DS-Lite backward compatibility

## Slide 4: Major Features
A simple extension for DS-Lite without centralized NAT
An address sharing mode for public 4over6
No IPv4 and IPv6 address coupling
  No extra requirement on address/prefix planning
  On-demand/pre-configured IPv4 address + port-set provision
Scalability through:
  Per-session=>per-subscriber state
    No per-flow state
  Minimal logging
tradeoff
Per-session stateful
stateless
Per-subscriber stateful

## Slide 5: Key points for per-subscriber stateful solution
Concentrator behavior
  For incoming IPv4 packets, use IPv4 dst addr & port to lookup binding table and retrieve IPv6 tunnel endpoint
  Packet encapsulation/de-encapsulation according to RFC2473
Initiator behavior
  Request IPv4 address + Port-set from DHCPv4-over-IPv6 Server
  Packet encapsulation/de-encapsulation, NAT within allocated port-set

## Slide 6: Per-Subscriber State Synchronization
Concentrator (AFTR)
DHCPv4
IPv6 | IPv4 | Port Range
2001:db8::1 | 192.1.2.3 | 1000-1999
2001:db8::2 | 192.1.2.3 | 2000-2999
Concentrator
AFTR Per-subscriber
mapping table
IPv6 | IPv4 | Port Range
2001:db8::1 | 192.1.2.3 | 1000-1999
2001:db8::2 | 192.1.2.3 | 2000-2999
DHCPv4 Per-subscriber
mapping table

## Slide 7: History
Lightweight 4over6-07
  Merge three documents
    I-D.cui-softwire-b4-translated-ds-lite
    I-D.zhou-softwire-b4-nat
    I-D.penno-softwire-sdnat-02
  Substantial edits
  Major updates:
    The I-D chose DHCP as the mandatory provisioning method
    Other provisioning methods are optional
    Improved ICMPv4 processing description

## Slide 8: Collaboration Team
Operators
Vendors
Notes: Currently, we have a large collaboration team. We have 7 operators from China Telecom, …
<number>

## Slide 9: Running Code/Test/Field Trial
We have published the source code on:
  http://sourceforge.net/projects/laft6/
We already have run field trial/test in:
  China Telecom
  Deutsche Telekom
  CERNET2
  Freebit
We already have products from Yamaha, and we will soon have commercial products from Huawei and Juniper.
Notes: <number>

## Slide 10: China Telecom Field Trial
IPv4 server
Access
Network
(IPv6)
Metro Network
(IPv6)
Backbone
(IPv4)
Backbone
(IPv6)
IPv6 server
BR
BR
BRAS (DHCPv6)
lw4over6
Concentrator
lw4over6
Initiator
Dual-stack user
IPv4-only user
syslog system
NE40e
Notes: <number>

## Slide 11: Next Steps
Comments?
Call for WG adoption?