## Slide 1: 4rd Implementation Report
Bing Liu(speaker), Sheng Jiang, Yu Fu
@softwire-IETF 84-Vancouver
Aug-2 2012

## Slide 2: 4rd logical functions (CPE)
4o6报文 解/封装
IPv6转发模块
CPE
4rd BR
IPv4转发模块
IPv4/IPv6 判断模块
IPv4 host
IPv6 host
NAT44 翻译
端口 限制
4->6
translation
IPv6
forwarding
CPE
IPv6
only
Identifying
4rd packets
NAT44
Addr
Calculation
Port
restrict
IPv4
Fragmt
Mapping
rule table
Fragmt Hdr
6->4
translation
Fragmt Hdr
IPv4
Forwarding

## Slide 3: 4rd logical functions (BR)
Identififying
4rd packets
IPv6 FWD
CPE
Addr
Calculation
IPv6
only
IPv4
FWD
IPv4 Internet
IPv6 Internet
Mapping
rule table
6->4
4->6
IPv4
Fragmt
Frag Hdr
Frag Hdr

## Slide 4: Implementation in Linux
Linux Kernel TCP/IP Stack
CPE LAN
Interface
4RD
Virtual Interface
CPE WAN
Interface
4RD Translator
Linux Kernel Netfilter
4rd module

## Slide 5: Preliminary Conclusions
4rd doesn’t change any IP protocol standards at the routing plane.
At the routing plane, 4rd packet is identical to normal IPv6 packet. Since we only used standard interfaces to input/output packets to/from the 4rd module, the TCP/IP stack itself doesn’t need to do 4rd-specific extension.
The 4rd fragment header remains the same data structure of IPv6 standard, the utilization of fragment-header doesn’t bother the TCP/IP stack and routers, unless fraghdr-specific-rules DPI is deployed.
4rd packet translation is lightweight
No need to deal with the checksum adjustment(benefit from CNP)
No need to process each protocol (TCP/UDP/ICMP) respectively
More likely an “encapuslation” rather than “translation”
    Our implementation and analysis haven’t identified any ambiguity or flaw.

## Slide 6: Thank you! leo.liubing@huawei.com jiangsheng@huawei.com eleven.fuyu@huawei.com Aug 2, @Vancouver