## Slide 1: MAP Testing Results
X. Li, C. Bao, G. Han, W. Dec
2012-07-28

## Slide 2: Testing topology

## Slide 3: Address format

## Slide 4: MAP-T
DMR
  utils/ivictl -r -d -P 2001:da8:b4b6:ffff::/64 –T
BMR
  utils/ivictl -s -i eth1 -I eth0 -H -N -a 192.168.1.0/24 –A 202.38.117.1/24 -P 2001:da8:b4b6::/48 -R 16 -M 2 -o 0 -c 1440 -T
tcpdump
  09:42:16.526809 IP6 2001:da8:b4b6:100:ca:2675:100:0 > 2001:da8: b4b6:ffff:ca:7023:fe00:0: ICMP6, echo request, seq 18177, length 40
  09:42:16.527448 IP6 2001:da8:b4b6:ffff:ca:7023:fe00:0 > 2001:da8: b4b6:100:ca:2675:100:0: ICMP6, echo reply, seq 18177, length 40
Native IPv6 packets are marked blue (the next header is ICMPv6)

## Slide 5: MAP-E
DMR
  utils/ivictl -r -d -P 2001:da8:b4b6:ffff:1234::5678/128 -E
BMR
  utils/ivictl -s -i eth1 -I eth0 -H -N -a 192.168.1.0/24 -A 202.38.117.1/24 -P 2001:da8:b4b6::/48 -R 16 -M 2 -o 8 -c 1400 -E
tcpdump
  09:38:43.326429 IP6 2001:da8:b4b6:180:ca:2675:180:0 > 2001:da8: b4b6:ffff:1234::5678: IP 202.38.117.1 > 202.112.35.254: ICMP echo request, id 1040, seq 32512, length 40
  09:38:43.327786 IP6 2001:da8:b4b6:ffff:1234::5678 > 2001:da8:b4b6: 180:ca:2675:180:0: IP 202.112.35.254 > 202.38.117.1: ICMP echo reply, id 1040, seq 32512, length 40
IPv6 packets are marked red (the next header is IP), encapsulated IPv4 packets are marked blue

## Slide 6: Mixed MAP-T/MAP-E
BR=T/CE=E
  09:39:48.829067 IP6 2001:da8:b4b6:180:ca:2675:180:0 > 2001:da8: b4b6:ffff:1234::5678: IP 202.38.117.1 > 202.112.35.254: ICMP echo request, id 1040, seq 47104, length 40
  09:39:48.833054 IP6 2001:da8:b4b6:ffff:ca:7023:fe00:0 > 2001:da8: b4b6:180:ca:2675:180:0: ICMP6, echo reply, seq 47104, length 40
BR=E/CE=T
  09:44:11.692130 IP6 2001:da8:b4b6:100:ca:2675:100:0 > 2001:da8: b4b6:ffff:ca:7023:fe00:0: ICMP6, echo request, seq 41473, length 40
  09:44:11.693044 IP6 2001:da8:b4b6:ffff:1234::5678 > 2001:da8:b4b6: 100:ca:2675:100:0: IP 202.112.35.254 > 202.38.117.1: ICMP echo reply, id 1024, seq 41473, length 40
the forwarding mode configuration is only required in the IPv4 to IPv6 direction, it can be automatically identified by checking the value of the next header in the IPv6 packets in the IPv6 to IPv4 direction

## Slide 7: Backward Compatibility: DS-lite
DMR
  utils/ivictl -r -d -P 2001::1/128
BMR
  utils/ivictl -s -i eth1 -I eth0 -H -N -X -a 192.168.1.0/24 -A 10.255.255.1/24 -P 2001:da8:b001:1009::/64 -R 16 -M 2 -o 0 -c 1400 -E
tcpdump
  22:48:42.536559 IP6 2001:da8:b001:1009:a:ffff:100:0 > 2001::1: IP 10.255.255.1 > 202.112.35.254: ICMP echo request, id 1024, seq 41473, length 40
  22:48:42.539352 IP6 2001::1 > 2001:da8:b001:1009:a:ffff:100:0: IP 202.112.35.254 > 10.255.255.1: ICMP echo reply, id 1024, seq 41473, length 40

## Slide 8: Backward Compatibility: NAT64
DMR
  utils/ivictl -r -d -P 2001:da8:b4b6:1000::/64 -T
BMR
  utils/ivictl -s -i eth1 -I eth0 -H -N -X -a 192.168.1.0/24 -A 2.2.2.2/32 -P 2001:da8:b001:fff9::/64 -R 16 -M 2 -o 0 -c 1440 -T
tcpdump
  09:24:16.478385 IP6 2001:da8:b001:fff9:2:202:200:0 > 2001:da8: b4b6:1000:ca:7023:fe00:0: ICMP6, echo request, seq 25600, length 40
  09:24:16.479638 IP6 2001:da8:b4b6:1000:ca:7023:fe00:0 > 2001:da8: b001:fff9:2:202:200:0: ICMP6, echo reply, seq 25600, length 40

## Slide 9: Conclusions
A unified MAP can support MAP-T, MAP-E and even the mixed modes without introducing additional complexity
  5,000 lines total, 200 lines difference (4%)
A unified MAP CE can be configured backward compatible with stateful NAT64 and dual-stack lite
  Ecdysis nat64
  Aftr-1.1

## Slide 10: References
[dual-stack-lite-code] "Dual-stack Lite Code: http://www.isc.org/software/aftr/11".
[map-code] "MAP Code: http://mapt.ivi2.org:8039/mapt.html".
[nat64-code] "NAT64 Code: http://ecdysis.viagenie.ca/download.html".