## Slide 1: A Taxonomy of SIP B2BUAs draft-kaplan-straw-b2bua-taxonomy
tax-man: Hadriel Kaplan

## Slide 2: The Problem(s)
To write a STRAW doc, we need to define what “types” of B2BUAs the doc applies to
We could do this in every doc, or we could do it in one doc: a Taxonomy
BUT, there may still be some STRAW docs that need to define special cases or sub-types
  For example, a B2BUA that handles IPv6-IPv4 interworking may need to have different requirements than one that does only IPv4 or IPv6

## Slide 3: So how many B2BUA types are there?
Too many – this WG can’t define them all
  (we don’t even know them all!)
But really we don’t need to list them all – just the major/basic types that would make a difference for STRAW stuff
    E.g: relays media or not, transcodes media or not, acts like Proxy vs. full UA for headers, etc.
So I’ve chosen to differentiate based on what “layer” the B2BUA operates at/on

## Slide 4: The not-so-OSI B2BUA layer model
Physical
Data-link
IPv4
IPv6
UDP
TCP
SCTP
TLS
Cleartext
Via/RR-proxy
Via/RR-replace
Contact-replace
Full SIP UAS-UAC
Media relay
SRTP Termination
Transcoding
Media generation
Skynet/Siri
Impacts more stuff in STRAW
Media layer B2BUAs
Signaling layer B2BUAs
Proxy-B2BUA
Signaling-only
B2BUA
Media-Relay B2BUA
Media-aware B2BUA
Media-termination
B2BUA

## Slide 5: Proxy-B2BUA
This is a pure RFC-3261 Proxy, except...
  It maintains enough state info to send in-dialog requests
  Example: terminate a dialog by sending a BYE, or send UPDATE/re-INVITE to check liveness
Does not modify headers/bodies
  Except inserts Via/Record-Route, decrements Max-Forwards, etc., per 3261

## Slide 6: Signaling-only B2BUA
May replace any/all headers, terminates/processes REFER, modifies specific bodies, etc.
  I.e., an App Server or non-media PBX
Does NOT touch media
  Does not modify SDP

## Slide 7: Media-relay B2BUA
A middlebox that relays UDP/TCP “media” packets, understands and modifies SDP
  i.e., a plain-vanilla media-proxy
Does NOT look into RTP/RTCP, does not transcode, terminate SRTP, munge RTP/RTCP, etc.
  If it does that, it’s a media-aware or media-termination B2BUA

## Slide 8: Media-Aware B2BUA
A middlebox that knows it’s relaying RTP/RTCP, looks into them for quality stats, or terminates SRTP
  i.e., most common SBC role
Does NOT transcode nor act as a B2BUA at the RTP/RTCP layer

## Slide 9: Media-termination B2BUA
A middlebox that is a B2BUA for media, such as transcodes
  This is the full shebang
  This would be a PSTN gateway, except the context of a B2BUA would be SIP on both sides so PSTN Gateway wouldn’t apply

## Slide 10: Open Issues
Should we classify Conference Servers as B2BUAs for STRAW?
  Right now they’re not really, because they’re typically multiple UAS’, not a UAS-UAC pairing
Are the type names and descriptions ok?
Is the doc going in the right direction? (who’s read it?)