## Slide 1: Shared Use of TCP Experimental Options
07/31/26 07:09
<number>
draft-ietf-tcpm-experimental-options-01
IETF 84
Joe Touch, USC/ISI

## Slide 2: Summary
Current experimental options overloaded
  Multiple concurrent uses cannot be distinguished
Add nonce to EO format
  Nonce used to differentiate concurrent uses
Goal
  Proposed Standard, as per WG direction
07/31/26 07:09
<number>

## Slide 3: Changes 00->01
All based on WG recommendations:
  Wording
    Use “magic number” rather than “nonce”
    Use “codepoints” throughout
  Length SHOULD be 32, but MAY be longer or shorter
  Location MUST be in SYN, SHOULD be used anywhere the option is present
Other additions:
  Impact of false positives discussed, with mitigation
  Migration plan discussion (still notes that this is up to the option designer)
07/31/26 07:09
<number>

## Slide 4: Current Status
No pending issues
  One question off-list regarding use of existing experimental codepoints vs. new ones
  Referred to the WG discussion on this (no benefit to new codepoints, just encourages misuse of existing codepoints)
Awaiting WGLC
07/31/26 07:09
<number>

## Slide 5: A TCP Authentication Option NAT Extension
07/31/26 07:09
<number>
draft-touch-tcp-ao-nat-03
IETF 82
Joe Touch, USC/ISI

## Slide 6: Summary
Experimental extension to TCP-AO for NATs
  Change to packet processing to allow use of TCP-AO in NAT/NAPT environments
  Relies only on endpoint agreement
Submitted for individual publication 6/12
  Insufficient WG interest, so already proceeded as individual
07/31/26 07:09
<number>