## Slide 1: RFC1323bis – TCP Extensions for High Performance
Richard Scheffenegger (Editor)
David Borman
Bob Braden
Van Jacobson

## Slide 2: RFC1323bis
20 years since adoption of RFC1323
New revision started in 5 years ago
WG Item quite some time (4 years)
Shepherd document to finish line
Two updates -02 and -03

## Slide 3: Changes since draft-ietf-tcpm-1323bis-01
Changed format from noff to xml2rfc
  addressed some nits around indentation
  new citation and TOC style
  removed references to historic RFC1072
  Caret ^ instead of C-style ** for exponential notation

## Slide 4: Changes since draft-ietf-tcpm-1323bis-01
Content:
  Window Scale (WS):
    sec 2.4 window retraction – M. Mathis
  Timestamp (TS):
    sec 3.2 removed text to allow potential in-session negotiation of TS – M. Mathis
    sec. 3.3 explicitly excluding ACKs with selective acknowledgements (SACK) for round trip-time measurement (RTTM) processing – R. Scheffenegger
Lots of typos and inconsistencies
  Thanks to A. Hoenes, A. Zimmermann

## Slide 5: Open in draft-ietf-tcpm-1323bis-03
RFC2119 BCP wording
Text around Nyquist criteria
    Delay in a packet network is not a time-continuous function (A. Hoenes)
Protection against wrapped sequence numbers (PAWS) check criteria
    discarding of reordered, pure ACKs
    no effect on reverse data (A. Zimmermann)
Processing Order
    e.g. pure ACK dropped by PAWS but may be interesting for RTTM, SACK,.. increases attack surface
Middlebox issues (Window Scale)

## Slide 6: Poll around draft-ietf-tcpm-1323bis-03
Who has read either -02 or -03 draft?
Objections to format, style?
Objections to modified content?
Feedback around open points?
Ready for WGLC (after RFC2119 update)?

## Slide 8: Backup

## Slide 9: Window Scale Retraction
Expanded text to dedicated section 2.4
Explicitly quoted section 4.2.2.16 of RFC1122 to describe the expected behavior.

## Slide 10: Timestamp negotiation
Allow late negotiation:
Old:
A TCP may send the Timestamps option (TSopt) in an initial <SYN> segment (i.e., a segment containing a SYN bit and no ACK bit), and may send a TSopt in other segments only if it received a TSopt in the initial <SYN> or <SYN,ACK> segment for the connection.
New:
A TCP may send the Timestamps option (TSopt) in an initial <SYN> segment (i.e., a segment containing a SYN bit and no ACK bit).

## Slide 11: Timestamp RTTM processing
Only reflect timestamp from last in-sequence data packet.
Only process timestamp when new data is acknowledged.
However, ACK loss may lead to increased RTT (first ACK in a series of duplicates lost)
Presence of SACK option indicates that reordering/loss was present at the receiver, sender SHOULD ignore that RTT update.