## Slide 1: TRILL: Traffic engineering draft-hu-trill-traffic-engineering-00.txt
Fangwei Hu hu.fangwei@zte.com.cn
Jacni Qin jacni@jacni.com
Donald Eastlake 3rd d3e3e3@gmail.com
Radia Perlman Radia@alum.mit.edu

## Slide 2: TRILL TE
TE(Traffic Engineering) is a flexible technique that can enhance the performance of an operational network at both the traffic and resource.
Extension to support TE in TRILL campus

## Slide 3: Overview
An RBridge that is the egress for a traffic engineered route holds an extra nickname which is for TE use.
Regular traffic has a regular nickname as egress and follows a least cost route
TE traffic has a TE nickname as egress and follows a TE route

## Slide 4: Overview
TE path can be statically configured or calculated based on the TE metrics carried by sub-TLVs inside ISIS TLV 22
The basic routing path and TE routing path share the same forwarding table

## Slide 5: Comparison of TE with MT
MT:
  Constrain frames in a particular topology
  Support Multi destination and unicast frame
  The number of available topologies is limited
TE:
  Only support unicast frame
  The TE path can be configured or computed based on TE cost
  Can support a large number of TE paths

## Slide 6: Comparison with layer 3 IS-IS TE
TRILL TE:
  Very simple in implementation
  No complicated signal protocol
  No explicitly tunnels
  "TE Router ID TLV for TRILL" is not required
Layer 3 IS-IS TE:
  Use Router ID TLV(TLV 134)
  Signal protocol

## Slide 7: TRILL TE Nickname
There are no flag bits available in the Nickname sub-TLV
There are several reasons to mark nicknames (or blocks of nicknames)
  Nickname is for TE use
  Nickname will be used as ingress (to reduce RPFC state)
  Nickname is allowed/prohibited for use in campus or level 1 area…

## Slide 8: END