## Slide 1: TRILL Resilient Distribution Trees
draft-zhang-trill-resilient-trees-00.txt
Mingui Zhang
Tissa Senevirathne
Janardhanan Pathangi
Ayan Banerjee
Notes: TRILL Resilient Distribution Trees

## Slide 2: When a Distribution Tree Fails
A broken distribution tree (DT) is recovered through campus wide re-convergence.
It may lead to considerable long disruption to ongoing multicast traffic.
Protection mechanisms should be designed to mitigate this disruption.
How to realize this kind of protection?

## Slide 3: Usage of Affinity TLV
Explicitly assign a link on a DT
  It is called “Affinity Link” in this doc
An Affinity Link is not necessarily on the shortest path.
Actually, Affinity TLV provides a way to manipulate distribution tree calculation.

## Slide 4: DT Calculation with the Affinity TLV
Suppose the Affinity Link is RB4->RB5, tree root is RB1
  {Nickname=RB5, Num of Trees=1, Tree-num of roots=RB1}
Delete all other in-links except RB4->RB5
Compute the DT according to SPF calculation
Link RB4->RB5 will surely appear on the DT
RB3
RB2
RB1
RB6
RB5
RB4
RB3
RB2
RB1
RB6
RB5
RB4
1
4
2
5
3
6
Full Graph
Sub Graph
DT
Notes: This slide tells us how an Affinity Link is carried out in the distribution tree calculation.

## Slide 5: Protecting a Link Connecting Edge RBs
RB1, root
RB2
RB5
RB4
RB3
RB1
RB2
RB5
RB4
RB3, root
primary tree
backup tree
Link RB2-RB4 on the primary tree is protected by the backup tree.
Affinity Link

## Slide 6: Protecting a Link between Intermediate RBs
RB1, root
RB2
RB5
RB4
RB3
RB1
root, RB2
RB5
RB4
RB3
primary tree
backup tree
Link RB1-RB3 on the primary tree is protected by the backup tree.
Affinity Link

## Slide 7: Maximally Edge Disjoint DTs
The more Affinity Links are intentionally assigned, the more links of the backup DT can be pinpointed. Maximally disjoint primary & backup DTs can be set up in this way.
root
root
Full topology
tree1
tree2
o yellow and blue edges are disjoint.

## Slide 8: Multicast FRR using backup DT
Akin to the IGP multicast FRR
The backup DT is Installed in advance.
If a link on the primary DT fails and this failure does not affect the backup DT, use the backup DT directly to save the time on DT calculation and installation.

## Slide 9: Global 1:1 Protection
Suppose RB7 is the multicast source while RB9 and RB10 are the receivers.
When RB1-RB5 fails, RB7 will switch over the multicast traffic from tree1 to tree2.
root
root
RB1
RB3
RB6
RB7
RB9
RB10
RB7
RB9
RB10
RB3
RB5
RB6
RB1
RB2
pruned primary tree1
pruned backup tree2
RB5
Notes: The first protection mechanism is the 1 to 1 global protection.

## Slide 10: Global 1+1 Protection
RB7 replicates multicast frames and send them along both trees. Receivers RB9 & RB10 accept only one copy from the primary tree using RPFC.
When RB1-RB5 fails, RB9&RB10 change their RPFC and accept the other copy from the backup tree.
root
root
pruned primary tree1
RB1
RB3
RB5
RB6
RB7
RB9
RB10
pruned backup tree2
RB7
RB9
RB10
RB3
RB5
RB6
RB1
RB2

## Slide 11: Local Protection
When RB1-RB5 fails, RB1 locally switches over to the backup tree. Inject multicast traffic on behalf of RB7.
RPF relax is necessary.
  E.g., {root=RB2, ingress=RB7, incoming interface=RB1-RB2}
RPF relax can be dangerous. So, not recommended.
root
root
RB1
RB3
RB6
RB7
RB9
RB10
RB7
RB9
RB10
RB3
RB5
RB6
RB1
RB2
pruned primary tree1
pruned backup tree2
RB5

## Slide 12: Back to the Primary DT
When re-convergence finishes, RBridges SHOULD switch back to the new primary distribution tree.
RBridges then stop using the old backup DT.
The backup DT will be updated according to the new primary DT.

## Slide 13: Next Step
Call for WG adoption

## Slide 14: Thanks!